## Slide 1
Prof. Jongouk Choi
University of Central Florida
Spring 2026
CDA 5106: Advanced Computer
Architecture
Lecture 6: ILP

## Slide 2: Objectives and Outline
Objectives:
  Understand key Instruction Level Parallelism (ILP): superscalar and out-of-order scheduling
Outline:
  Dynamic or out-of-order (OOO) scheduling: instructions don’t have to execute in original program order
  Scoreboarding
  Tomasulo’s algorithm

## Slide 3: Module 6.1: Overview And CDC-6600 (scoreboarding)

## Slide 4: Objectives and Outline
Objectives:
  Understand the concept of dynamic or out-of-order scheduling of instructions
Outline:
  Problem with static scheduling
  Scheduling instructions based on the availability of data (dataflow)
  Decoupling Decode into Dispatch + Issue stages
  Dynamic scheduling in CDC-6600 architecture

## Slide 5: Overview
Dynamic or Out of Order (OOO) scheduling
  Expose more parallelism by ignoring artificial serial constraints of “sequential” program (insight: instructions don’t have to execute in original program order)
  Early machines: CDC-6600 and IBM 360/91
Register renaming
  Often used with dynamic scheduling
Precise interrupts
  Why we care about precise interrupts
  Reorder buffer
Superscalar and VLIW processors
  Fetch and execute more than 1 instruction each cycle

## Slide 6: True data dependences
Consider simple DLX pipeline
  Most operations take only 1 cycle to execute
  Bypasses handle most RAW hazards optimally (i.e., no stalls)
  Loads are a problem
    Cache hit: 2 cycles (EX generates address, MEM loads data)
    Cache miss: takes forever
    Data dependent instruction must stall
    Worse: the entire pipeline stalls, even other independent instructions
Longer latencies make matters worse
  E.g., floating-point operations
Superscalar processing makes matters worse
  Even with short latencies, long serial dependence chains limit parallelism
Notes: Following instructions can be stalled by the anti-dependent instruction stall

## Slide 7: Dynamic scheduling
Lessen impact of true data dependences
  Only data dependent instructions must wait for data (stall)
  Independent instructions after the dependent ones don’t stall if their data is available
  Execute instructions in the order specified by true data dependences, not the artificial program order
  Dataflow graph defines execution order
  Divide takes many cycles: stall the dependent ADDD but not the independent SUBD
  OOO execution allows SUBD to execute before ADDD
DIVD F0 , F2, F4
ADDD F10, F0, F9
SUBD F8 , F8, F14
Program fragment
DIVD
ADDD
SUBD
Dataflow Graph
Notes: Andi-dependent, and independent

## Slide 8: Pipeline modification
Fundamental pipeline change needed
  Stalled dependent instructions cannot block later independent instructions
  Split ID (decode stage) into two new stages
    DISPATCH (ID): instruction dispatch
    ISSUE (IS): instruction schedule / issue
  The ISSUE stage buffers instructions waiting (stalled) for data
  This allows later instructions to make progress (FETCH and DISPATCH are not stalled)
Notes: Issue stage has buffers
Keep instructions

## Slide 9: Pipeline modification
Simple in-order pipeline
Stalled instruction has no where to go
  Stalls in decode (ID) stage
  This stalls later instruction in IF
IF
ID
EX
MEM
WB

## Slide 10: Pipeline modification
Out-of-order pipeline
  Two decoupled pipelines:
    FETCH/DISPATCH pipeline brings instructions into processor in program order: scan instructions in program order – required to determine data dependences
    ISSUE/EXECUTE pipeline executes instructions based on data dependences and available functional units (FU)
IF
ID
FU
FU
FU
IS
EX
WB
fetch/dispatch
issue/execute

## Slide 11: High-level view
Out-of-order pipeline
  Two decoupled pipelines: fetch/dispatch and issue/execute
  Pipelines decoupled by buffers
    Many names: reservation stations, issue queues/buffers, scheduling queues or “instruction window”
Instruction
issue/execute
pipeline
Instruction
fetch/dispatch
pipeline
fetch
decode
data dependence checking,
register renaming
DISPATCH
ISSUE
(insert into window)
(take from window)
WINDOW
issue
execute
complete (writeback)
In-order
Out-of-order

## Slide 12: Early dynamically scheduled machines
CDC-6600
  Centralized control: “CDC scoreboard”
  Many replicated functional units
  All values pass through the register file
  Stall on WAR/WAW hazards
Next Module: IBM 360/91 (Tomasulo’s algorithm)
  Distributed control: “reservation stations”
  Several, fully-pipelined functional units (equivalent to replicating functional units)
  Values broadcast to waiting instructions and register file in parallel (via the Common Data Bus)
  Introduced register renaming: handles WAR/WAW hazards without stalling

## Slide 13: CDC-6600 (DLX version)
Four stages after fetch
  Dispatch
    Check for structural and WAW hazards
      Structural: stall in dispatch stage if FU busy
      WAW: stall in dispatch stage if an outstanding instruction in the scoreboard writes the same destination register
    Enter instruction into scoreboard: determine data dependences
    Route instruction to a free FU, where it waits until data operands are available
  Issue
    Wait for operands to become ready
    Scoreboard signals when operands ready
      Instruction reads registers from the register file
      Then issues to FU for execution
  Execute
  Write result
    Check for WAR hazard: stall if an outstanding, prior instruction in the scoreboard reads the same register being written, and the read has not yet taken place
Notes: Functional Unit • A computer in its simplest form comprises of five functional units namely input unit, output unit, memory unit, arithmetic & logic unit and control unit.
If no structural, WAW hazard, then go to scoreboard for data dependence check
WAR, cache miss…read takes more cycles…

## Slide 14: Aside: Warning – H&P naming
H&P uses different names than what we will use
  US: dispatch THEM: issue (ugh!)
  US: issue THEM:read operands (this does occur)
  US: execute THEM: execute
  US: write result THEM: write result

## Slide 15: CDC-6600 (DLX version)
REGISTERS
FP MULT (1)
FP MULT (2)
FP DIV
FP ADD
Integer Unit (integer DLX pipeline)
SCOREBOARD
control/status
control/status
Notes: Scoreboard hazard detection unit,
Control FU and registers
Traffic signal regulate
When

## Slide 16: Scoreboard
Three data structures
  Instruction Status
    Which stage is the instruction in
  Functional Unit Status
    Busy - FU is busy executing another instr.
    Op - what instr. is the FU busy with
    Fi - destination register
    Fj, Fk - source registers
    Qj, Qk - func. units producing source regs
    Rj, Rk - flags indicating src regs are ready
  Register Result Status
    Which FU is going to write each register

## Slide 17: Running example
Example used for CDC and Tomasulo
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2

## Slide 18: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F6 | R2 |  |  |  | yes | 
MULT1 | no |  |  |  |  |  |  |  | 
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
 |  |  | integer |  |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 19: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F6 | R2 |  |  |  | yes | 
MULT1 | no |  |  |  |  |  |  |  | 
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
 |  |  | integer |  |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 20: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F6 | R2 |  |  |  | no | 
MULT1 | no |  |  |  |  |  |  |  | 
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
 |  |  | integer |  |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 21: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F6 | R2 |  |  |  | no | 
MULT1 | no |  |  |  |  |  |  |  | 
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 22: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | yes | 
MULT1 | no |  |  |  |  |  |  |  | 
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
 | integer |  |  |  |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 23: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x | x |  | 
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | yes | 
MULT1 | yes | MULTD | F0 | F2 | F4 | Integer |  | no | yes
MULT2 | no |  |  |  |  |  |  |  | 
ADD | no |  |  |  |  |  |  |  | 
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
multi | Integer |  |  |  |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 24: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x | x | x | 
x |  |  | 
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | no | 
MULT1 | yes | MULTD | F0 | F2 | F4 | Integer |  | no | yes
MULT2 | no |  |  |  |  |  |  |  | 
ADD | yes | SUBD | F8 | F6 | F2 |  | Integer | yes | no
DIV | no |  |  |  |  |  |  |  | 
F0 | F2 | F4 | F6 | F8 | F10 | F12
multi | Integer |  |  | add |  | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 25: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x | x | x | 
x |  |  | 
x |  |  | 
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | no | 
MULT1 | yes | MULTD | F0 | F2 | F4 | Integer |  | no | yes
MULT2 | no |  |  |  |  |  |  |  | 
ADD | yes | SUBD | F8 | F6 | F2 |  | Integer | yes | no
DIV | yes | DIVD | F10 | F0 | F6 | MULT1 |  | no | yes
F0 | F2 | F4 | F6 | F8 | F10 | F12
multi | Integer |  |  | add | divide | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 26: Remaining bottlenecks
CDC-6600 does good job of dynamic scheduling around RAW hazards
Remaining performance limitations
  Amount of instruction-level parallelism (ILP) in the program
    Are there sufficient data-independent operations?
    Needs large window to look farther ahead
    Requires branch prediction to support large window
  Number of scoreboard entries (window size)
    Dictates how far processor can look ahead
  Number and type of functional units, register ports, etc.
    Structural hazards
    Lengthy binding of FU to Instruction
  Anti- and output dependences
    Dynamic scheduling exposes more WAW+WAR hazards because early (OOO) writes are possible
    WAR made worse in CDC due to late reads (read operands when finally issuing – even when operands were ready some time ago)
    WAW handled like a structural hazard in dispatch

## Slide 27: Module 6.2: OoO execution (Tomasulo’s algorithm)

## Slide 28: RECAP: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x | x | x | 
x |  |  | 
x |  |  | 
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | no | 
MULT1 | yes | MULTD | F0 | F2 | F4 | Integer |  | no | yes
MULT2 | no |  |  |  |  |  |  |  | 
ADD | yes | SUBD | F8 | F6 | F2 |  | Integer | yes | no
DIV | yes | DIVD | F10 | F0 | F6 | MULT1 |  | no | yes
F0 | F2 | F4 | F6 | F8 | F10 | F12
multi | Integer |  |  | add | divide | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example

## Slide 29: Objectives and Outline
Objectives:
  Understand the foundation of out-of-order scheduling: Tomasulo algorithm
Outline:
  Key aspects of Tomasulo and differences vs. CDC-6600
  Pipeline stages and structures in Tomasulo (operation queues, reservation stations, common data bus)
  Register renaming as a key technique to remove WAR/WAW dependences and hazards
  Step by step illustration of Tomasulo’s algorithm

## Slide 30: Tomasulo’s Algorithm
Born of necessity
  Used in IBM 360/91 floating-point unit
  Many long-latency operations
    Need dynamic scheduling: mitigate long stalls
  ISA specified only 4 floating-point registers
    Need register renaming: with only 4 registers, WAW/WAR hazards pop up quickly
    Especially in floating-point code: loops by definition cause repeated writes to same registers
    Renaming: recognize and give unique names to different dynamic instances of the same register specifier

## Slide 31: Key aspects of Tomasulo’s Alg.
Read register operands at dispatch stage
  If operands are available, the data is buffered along with the instruction in “reservation stations”
  CDC: only buffers the instruction, all operands are read from register file when all operands are ready (operands read at issue stage)
  CDC – late reads / Tomasulo – early reads: early reads help WAR condition
Unavailable registers are renamed at dispatch stage
  Waiting instructions replace register specifiers with a “tag” indicating the producer instruction
  Register specifiers are used only once, at dispatch!
  Renaming eliminates WAR/WAW hazards
Successive writes to a register
  Only last one is actually used to update register: helps WAW condition
  CDC: stall in dispatch until WAW hazard goes away

## Slide 32: Other differences with CDC
Distributed control
  Reservation stations (versus scoreboard)
Results broadcast to both register file and functional units
  Result bus called the “Common Data Bus” (CDB)
  Don’t have to wait for value to go through register file (i.e., use bypasses)
  Functional units don’t contend for register file ports

## Slide 33: 360/91 FP unit (DLX version)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)

## Slide 34: Tomasulo’s Alg. (DLX version)
Four stages after fetch
  Dispatch
    Check for structural hazard
      Stall in dispatch stage if no free reservation station
    Read register file
      Read data operands if available
      Read “tag” if data operand unavailable: a tag is the reservation station number of the producer instruction
    Route instruction plus data or tags to reservation station, where it waits until all operands are available
  Issue
    Wait until operands become available on the CDB (match CDB tag against operand tags)
    Grab operands from CDB and issue to FU (if free)
  Execute
  Write result
    Broadcast result + tag to all reservation stations, store buffers, and register file via the CDB
    Only write register file if the CDB tag matches the tag in the register file
Notes: Struc hazard: no free RS (rather than free FU!) so less structural hazard than CDC since num RSes > num FUs
Tomasulo has renaming (register operand index is renamed to RS index vs. CDC that has no renaming!)
Tomasulo uses bypassing using CDB where producer inst broadcasts its result to others in RS (CDC passes values through regsister files)
Tomasulo potentially supports OOO issue (since wakeup-select can be easily supported with RS)
Tomasulo uses reg file to store value or RS tag (for reg mapping), so if there are two insts writing to the same reg, the map will change to the
Latter inst. This means that the first inst will not write to reg file (it will just broadcast its result), while the second will write to reg file.

## Slide 35: Four stages (cont…)
Notice:
  Same four stages as CDC, but read register file at dispatch stage and replace register specifiers with tags
  No WAW / WAR checks (using tags eliminates these)
Again, H&P uses different names than what we will use
  Worse, H&P specifies only three stages for Tomasulo
  But any dynamic scheduling inherently has dispatch, issue, execute, write result…
Notes: Tag is just a new name of regiter specifier

## Slide 36: Register renaming
Consider simple example with register reuse
Dataflow graph with both true and false dependences
All instructions execute serially
  Due to reuse of F0 by the loads
  But those are 2 distinct instances of F0
  Use different names for 2 instances of F0
LD F0, 34(R2)
ADDD F4, F0, F2
LD F0, 45(R3)
ADDD F8, F0, F6
LD (1)
ADDD (1)
LD (2)
ADDD (2)
True dependence (RAW / F0)
True dependence (RAW / F0)
Anti-dependence (WAR / F0)
Output dependence (WAW / F0)

## Slide 37: Register renaming
Same program segment with F0 renamed
  Tomasulo Alg: use reservation station number (tag) of producer instruction (e.g. load buffer 1 = load1)
    This guarantees unique names for unique values
Dataflow graph with only true dependences
  Renaming removes output and anti-dependences
  Parallelism is exposed
LD load1, 34(R2)
ADDD F4, load1, F2
LD load2, 45(R3)
ADDD F8, load2, F6
LD (1)
ADDD (1)
True dependence (RAW / load1)
LD (2)
ADDD (2)
True dependence (RAW / load2)
LD (1)
ADDD (1)
LD (2)
ADDD (2)
True dependence (RAW / F0)
True dependence (RAW / F0)
Anti-dependence (WAR / F0)
Output dependence (WAW / F0)

## Slide 38: How (Tomasulo) renaming works (1)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
LD F0 <-
ADDD <- F0
LD F0 <-
ADDD <- F0
A
B
C
D
F0
LD load1, 34(R2)
ADDD F4, load1, F2
LD load2, 45(R3)
ADDD F8, load2, F6

## Slide 39: (2)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
load1
ADDD <- F0
LD F0 <-
ADDD <- F0
A
B
C
D
F0
load1
LD load1, 34(R2)
ADDD F4, load1, F2
LD load2, 45(R3)
ADDD F8, load2, F6

## Slide 40: (3)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
load1
LD F0 <-
ADDD <- F0
A
B
C
D
F0
load1
load1
(value)
LD load1, 34(R2)
ADDD F4, load1, F2
LD load2, 45(R3)
ADDD F8, load2, F6

## Slide 41: (4)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
load1
ADDD <- F0
A
B
C
D
F0
load2
load1
(value)
load2
LD load1, 34(R2)
ADDD F4, load1, F2
LD load2, 45(R3)
ADDD F8, load2, F6

## Slide 42: (5)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
load1
A
B
C
D
F0
load2
load1
(value)
load2
load2
(value)

## Slide 43: (6) Second load completes 1st
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
load1
A
B
D
F0
load1
(value)
load2
(value)
value2
value2
value2
C

## Slide 44: (7)
To memory
From memory
OPERAND
BUSES
OPERATION BUS
RESERVATION
STATIONS
FP adders
FP multipliers
LOAD
BUFFERS
STORE
BUFFERS
FLT. PT.
OPERATION
QUEUE
From IF unit
4 FP
REGISTERS
1
2
3
4
5
6
1
1
2
2
3
COMMON DATA BUS (CDB)
B
F0
load1
(value)
value1
value2
A
value1

## Slide 45
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |  |  |  |  |  | 
IF | ID | IS | EX | EX | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | IF | ID | IS | EX | EX | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | IF | ID | IS | IS | EX | EX | EX | EX | EX | EX | EX | EX | EX | EX | WB |  |  |  |  |  |  |  |  | 
 |  |  | IF | ID | IS | EX | EX | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | IF | ID | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | EX | ….. | ….. |  |  |  |  |  |  | 
 |  |  |  |  | IF | ID | IS | EX | EX | WB |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Recall our on-going example
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Shaded boxes indicate stalls.
RAW
1. LD-MULTD (F2)
2. MULTD-DIVD (F0)
1
2
=> Execution latencies: LD (2 – agen + access), MULTD (10), DIVD (40), SUBD/ADDD (2)
CDB:
F6
F2
F8
F6’
F0

## Slide 46: Aside: CDC-6600 example
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |  |  |  |  | 
ID | IS | EX | EX | WR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | ID | IS | EX | EX | WR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | ID | IS | IS | IS | IS | EX | EX | EX | EX | EX | EX | EX | EX | EX | EX | WR |  |  |  |  |  |  | 
 |  |  | ID | IS | IS | IS | EX | EX | WR |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ID | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | IS | EX | ….. | ….. |  |  | 
 |  |  |  |  | ID | ID | ID | ID | IS | IS | EX | EX | EX | EX | EX | EX | EX | EX | WR |  |  |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
=> Notice there are always 2 cycles between EX of data dependent instructions (e.g., LD and MULTD):
producer does WR and consumer does last IS cycle in which registers are read from the register file.
This is an artifact of the CDC-6600: all values must first pass through the register file (no bypasses).
Shaded boxes indicate stalls.
RAW
Structural
WAR
1. LD-MULTD (F2)
2. LD-SUBD (F2)
3. MULTD-DIVD (F0)
4. SUBD-ADDD (F8)
1
2
3
4
6
5
5. SUBD-ADDD (ADD unit)
6. DIVD-ADDD (F6)
=> Execution latencies: LD (2 – agen + access), MULTD (10), DIVD (40), SUBD/ADDD (2)
Load, subd/addd: 2 cycles
MULTD: 10 cycles
DIVD: 40 cycles
Notes: MULTD is delayed because of true dep, prior instruction first writes result (WR), then it reads operand (IS) before execution
SUBD has the same thing
DIVD depends on MULTD so it has to wait until MULTD finishes writing its result
Another problem: binding of inst to FU is early (dispatch) so the last ADDD suffers structural hazard for too long
Final problem: FU is bound to inst for too long (if there is a WAR dep), creating further structural hazards

## Slide 47: Tomasulo vs. Scoreboard
Is tomasulo better?
Finish in 17 cycles vs. 20 for scoreboard, why?
We do reach the divide 3 cycles earlier… Simultaneous read of operand for SUBD and MULT
Notes: Tomasulo finished in 59 cycles vs. 61 for CDC: problem is divide instruction takes too long (good example of Amdahl’s law)
However, we get to the divide 3 cycles earlier in Tomasulo’s algorithm than the CDC scoreboard.
Why?

## Slide 48: Further study…

## Slide 49: Module 6.3: Precise Interrupt and Reorder Buffer

## Slide 50: Objectives and Outline
Objectives:
  Understand the problem of precise interrupts
  Understand reorder buffer as a solution to the precise interrupt problem
Outline:
  Types of interrupts
  Correct handling of interrupts and why OOO execution may affect it
  Various approaches including reorder buffer (ROB)
  Tomasulo algorithm with ROB: mechanism and illustration
  Handling branch misprediction using precise interrupt mechanism

## Slide 51: Precise interrupts
Out-of-order execution and interrupts don’t mix!
  When an interrupt occurs, O/S wants precise state
  Precise state means:
    All instructions before the instruction causing the interrupt have completed
    All instructions after have not completed
  Why are precise interrupts important?
    O/S needs to save the state of the process and restart the process after servicing interrupt
      Restart occurs from the PC of interrupted instruction
      The restart state must reflect only changes up to that PC!
    Programmer debugging – user presumes sequential program
  Why is OOO-execution bad for precise interrupts?
    Instructions after interrupt may have updated state!

## Slide 52: Interrupts
Some examples
  “External interrupts”
    I/O device request
    Timer interrupt
    Power failing
  “Exceptions”
    Arithmetic overflow, divide-by-0, etc.
    Page fault
  “O/S calls”
    Also called system call or trap
    Initiated via an explicit instruction in ISA
External interrupts are asynchronous, exceptions are synchronous, O/S calls are synchronous and user-initiated

## Slide 53: Classifying Interrupts
Synchronous / Asynchronous
  Synchronous: function of program and memory state (e.g., arithmetic overfow, page fault)
  Asynchronous: external device or hardware malfunction (e.g., printer ready, bus error)
User request / Coerced
  From user program (O/S call – system call or trap)
  From O/S or hardware (e.g., page fault, protection violation)
User maskable / Nonmaskable
  User maskable: can be (temporarily) ignored (e.g., arithmetic overflow, breakpoint)
  Nonmaskable: must be handled (e.g., page fault, power fail)

## Slide 54: Classifying Interrupts (cont.)
Within an instruction / Between instructions
  Within: must be dealt with to complete an instruction (e.g., page fault)
  Between: not part of an instruction (e.g., I/O device request, O/S call)
Resume / Terminate
  Resume: must transparently return to user process (e.g., page fault, I/O device request)
  Terminate: give up and die (e.g., protection violation, power failure)

## Slide 55: Handling interrupts
Precise interrupts (Sequential Semantics)
  Complete instructions before offending one
  Squash (effects of) instructions after
  Save PC
  Force trap instruction into IF
Must handle simultaneous/OOO interrupts
  IF – memory problems (page fault, misaligned reference, protection violation)
  ID – illegal or privileged instruction
  EX – arithmetic exception
  MEM – memory problems (see IF above)
  WB – none
  Which interrupt should be handled first?

## Slide 56: Handling interrupts (cont.)
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  | 
i | IF | ID | EX | MEM | WB |  |  |  |  |  | 
i+1 |  | IF | ID | EX | MEM | WB |  |  |  |  | 
i+2 |  |  | IF | ID | EX | MEM | WB |  |  |  | 
i+3 |  |  |  | IF | ID | EX | MEM | WB |  |  | 
i+4 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
i+5 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
i+6 |  |  |  |  |  |  | IF | ID | EX | MEM | WB
Example: data page fault
Events
  Preceding instruction already complete
  Squash succeeding instructions
    Prevent from modifying state
  Inject ‘trap’ instruction, jumps to trap handler
  Trap handler saves precise state
page fault
squash
trap
trap handler

## Slide 57: Handling interrupts (cont.)
Out-of-order interrupts
  Example: which page fault should we take?
Answer
  Even though ‘i+1’ faults first, must service ‘i’ fault first
  Solution: post interrupts
    Check interrupt bit on entering WB
    This maintains precise interrupts
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  | 
i | IF | ID | EX | MEM | WB |  |  |  |  |  | 
i+1 |  | IF | ID | EX | MEM | WB |  |  |  |  | 
i+2 |  |  | IF | ID | EX | MEM | WB |  |  |  | 
i+3 |  |  |  | IF | ID | EX | MEM | WB |  |  | 
i+4 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
i+5 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
i+6 |  |  |  |  |  |  | IF | ID | EX | MEM | WB
page fault
page fault

## Slide 58: OOO-execution and interrupts
Preceding example assumed in-order pipeline
  WB occurs in-order
  This makes precise interrupts easy
Consider OOO-execution
  Problem: ADD has already completed, state is imprecise!
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  | 
MULTD F0, F2, F4 | IF | ID | IS | EX | EX | EX | EX | EX | WB |  | 
ADDD F6, F8, F8 |  | IF | ID | IS | EX | WB |  |  |  |  | 
floating-point arithmetic exception

## Slide 59: Solutions
Imprecise interrupts
  Ignore the problem
  Makes page faults difficult
  IEEE Standard strongly suggests precise interrupts
In-order completion
  Stall pipeline when necessary
Software clean-up
  Save information for trap handlers (pipeline state)
  Machine dependent
Hardware clean-up
  Restore consistent state
Re-order instructions
  Complete out-of-order
  Retire in-order
Can you tell which one is preferred?

## Slide 60: Reorder Buffer (ROB)
Operation of ROB
  ROB is a FIFO with head and tail pointer
  Instruction dispatch
    Reserve ROB entry at tail, advance tail ptr
    Record ROB entry (ROB tag) with instruction
  Instruction execution/completion
    Write value into ROB entry specified by the instruction’s tag
    DO NOT write result into the register file
    If instruction caused an exception, mark exception bit in the ROB for offending instruction
  Instruction retire (a.k.a. commit, graduate)
    Check instruction at the head of the ROB
      If completed, check exception bit
      If no exception, commit state (write value into register file) and advance head ptr
      If exception, squash subsequent instructions in ROB (back-up the tail ptr to the head ptr)

## Slide 61: New stage: Retire (RE)
IF
ID
IS
EX
WB
RE
in-order
out-of-order
in-order

## Slide 62: Reorder Buffer (cont.)
Entry | Dest | Result | Exception | Completed | PC
1 |  |  |  |  | 
2 | F6 |  | no |  | A
3 | F2 |  | no |  | B
4 | F0 |  |  |  | C
5 | F8 |  | no |  | D
6 | F10 |  |  |  | E
7 | F6 |  | no |  | F
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
… |  |  |  |  | 
ROB
HEAD
TAIL
Shown: The two loads (A and B) have completed and retired.
The MULTD has not completed.
The ADDD and SUBD have completed out-of-order, but the ROB prevents
them from retiring (updating state).
THUS: if the MULTD posts an exception, the Register File state is precise.
A LD F6 , 34(R2)
B LD F2 , 45(R3)
C MULTD F0 , F2, F4
D SUBD F8 , F6, F2
E DIVD F10, F0, F6
F ADDD F6 , F8, F2
dispatch
retire
update RF with value at head

## Slide 63: Precise Tomasulo Pipeline with ROB
Update state out-of-order: imprecise!
Register
File
Reservation
Stations
Functional
Units
1
2
Register
File
Reservation
Stations
Functional
Units
1
3
ROB
2
Complete out-of-order
Retire: Update state in-order: precise!
New bypass

## Slide 64: ROB requires bypass
Scenario
  Producer instruction completed – value in ROB
  Producer instruction not retired – value not in register file
  Then, dependent instruction is dispatched into window
    Value not read from register file
    Value can’t be grabbed from result bus – producer already completed!
    Only place data resides is in ROB – need to read value from ROB (ROB bypass)
    This new bypass is labeled (3) in previous diagram

## Slide 65
Entry | Dest | Result | Exception | Completed | PC
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | - | 54
 | - | 76
 | - | -5
 | - | -99
Reservation
Stations
R0
R1
R2
R3

## Slide 66: Example
A LW R2, 4(R0)
B MULT R3, R1, R2
C LW R2, 8(R0)
D ADD R1, R1, R2
E SUB R2, R0, R1
F ADD R0, R1, R2

## Slide 67
Entry | Dest | Result | Exception | Completed | PC
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | - | 54
 | - | 76
 | - | -5
 | - | -99
Reservation
Stations
R0
R1
R2
R3
A LW R2, 4(R0)

## Slide 68
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
0 |  | 54 |  | Imm=4
In RF | tag | value
 | - | 54
 | - | 76
 | 0 | -5
 | - | -99
Reservation
Stations
R0
R1
R2
R3
A LW R2, 4(R0)

## Slide 69
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
0 |  | 54 |  | Imm=4
In RF | tag | value
 | - | 54
 | - | 76
 | 0 | -5
 | - | -99
Reservation
Stations
R0
R1
R2
R3
B MULT R3, R1, R2

## Slide 70
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | - | 76
 | 0 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
B MULT R3, R1, R2
0 (cache miss)

## Slide 71
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
TAIL
HEAD
FUs
RF
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | - | 76
 | 0 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
C LW R2, 8(R0)
0 (cache miss)

## Slide 72
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 |  |  |  | C
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
2 |  | 54 |  | Imm=8
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | - | 76
 | 2 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
C LW R2, 8(R0)
TAIL
0 (cache miss)

## Slide 73
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 |  |  |  | C
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
2 |  | 54 |  | Imm=8
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | - | 76
 | 2 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
D ADD R1, R1, R2
TAIL
0 (cache miss)

## Slide 74
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 |  |  |  | C
3 | R1 |  |  |  | D
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
3 |  | 76 |  | 2
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 2 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
D ADD R1, R1, R2
TAIL
0 (cache miss)
2 (cache hit)

## Slide 75
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 |  |  |  | C
3 | R1 |  |  |  | D
4 |  |  |  |  | 
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
3 |  | 76 |  | 2
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 2 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
E SUB R2, R0, R1
TAIL
0 (cache miss)
2 (cache hit)

## Slide 76
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 |  |  |  | C
3 | R1 |  |  |  | D
4 | R2 |  |  |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
4 |  | 54 |  | 3
3 |  | 76 |  | 2
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
E SUB R2, R0, R1
TAIL
0 (cache miss)
2 (cache hit)

## Slide 77
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | no |  | C
3 | R1 |  |  |  | D
4 | R2 |  |  |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
4 |  | 54 |  | 3
3 |  | 76 |  | 666
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
2, 666, no exception

## Slide 78
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | no |  | C
3 | R1 |  |  |  | D
4 | R2 |  |  |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
4 |  | 54 |  | 3
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
3

## Slide 79
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | no |  | C
3 | R1 | 742 | No |  | D
4 | R2 |  |  |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
4 |  | 54 |  | 742
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
3, 742, no exception

## Slide 80
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
4, -688, no exception

## Slide 81
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 |  |  |  |  | 
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 0
In RF | tag | value
 | - | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
F ADD R0, R1, R2

## Slide 82
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 |  |  |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
5 |  | 742 |  | -688
1 |  | 76 |  | 0
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
F ADD R0, R1, R2

## Slide 83
Entry | Dest | Result | Exception | Completed | PC
0 | R2 |  |  |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 0
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0 (cache miss)
5, 54, no exception

## Slide 84
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
1 |  | 76 |  | 650000
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | -5
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
0, 650000, no exception

## Slide 85
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 |  |  |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | 650000
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R2, Tag=0, Val=650000
Note: tag doesn’t match RF tag, don’t set “In RF”
Note: commit value to register file state
1 (multiply)

## Slide 86: Two scenarios next…
Multiply
  Scenario #1: Completes without exception
  Scenario #2: Raises exception

## Slide 87
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | 650000
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
1, 49400000, no exception

## Slide 88
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | 650000
 | - | 49400000
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R3, Tag=1, Val=49400000
Note: tag matches RF tag, so set “In RF”
Note: commit value to register file state

## Slide 89
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | 666
 | - | 49400000
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R2, Tag=2, Val=666
Note: tag does not match RF tag, don’t set “In RF”
Note: commit value to register file state

## Slide 90
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | - | 742
 | 4 | 666
 | - | 49400000
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R1, Tag=3, Val=742
Note: tag matches RF tag, so set “In RF”
Note: commit value to register file state

## Slide 91
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | - | 742
 | - | -688
 | - | 49400000
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R2, Tag=4, Val=-688
Note: tag matches RF tag, so set “In RF”
Note: commit value to register file state

## Slide 92
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | 49400000 | No |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | - | 54
 | - | 742
 | - | -688
 | - | 49400000
Reservation
Stations
R0
R1
R2
R3
TAIL
Reg=R0, Tag=5, Val=54
Note: tag matches RF tag, so set “In RF”
Note: commit value to register file state

## Slide 93: Now do scenario #2

## Slide 94
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | - | Yes |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | 5 | 54
 | 3 | 76
 | 4 | 650000
 | 1 | -99
Reservation
Stations
R0
R1
R2
R3
TAIL
1, exception

## Slide 95
Entry | Dest | Result | Exception | Completed | PC
0 | R2 | 650000 | No |  | A
1 | R3 | - | Yes |  | B
2 | R2 | 666 | No |  | C
3 | R1 | 742 | No |  | D
4 | R2 | -688 | No |  | E
5 | R0 | 54 | No |  | F
6 |  |  |  |  | 
7 |  |  |  |  | 
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
11 |  |  |  |  | 
12 |  |  |  |  | 
13 |  |  |  |  | 
14 |  |  |  |  | 
15 |  |  |  |  | 
ROB
FUs
RF
HEAD
my tag | src1 ready | src1 tag/value | src2 ready | src2 tag/value
In RF | tag | value
 | - | 54
 | - | 76
 | - | 650000
 | - | -99
Reservation
Stations
R0
R1
R2
R3
TAIL

## Slide 96: Handling Branch Mispredictions
Branch mispredictions are like exceptions?
  Yes and No
  Handle exactly like exception (low performance)
    Wait until mispredicted branch reaches head of ROB
    Squash entire ROB, set all “In RF” bits
    Restart along correct path, no problem
    Delaying recovery until retirement is a big performance penalty
  Better performance
    Easy part: Squash bad instructions immediately by moving ROB tail pointer to just after branch entry
    Hard part: Restore register file tags to their state before the branch so that renaming restarts correctly
    How? Checkpoint register file tags at every branch instruction. Restore tags from checkpoint when misprediction detected.

## Slide 97: Module 6.4: ILP 4, History Buffer, Future File, Memory Dependences and Ordering

## Slide 98: Objectives and Outline
Objectives:
  Understand variations of ROB: history buffer and future file
  Understand how memory dependences are handled with OOO scheduling
Outline:
  History Buffer and Future File
  Memory dependences: WAW, WAR, RAW
  Handling loads and stores in the pipeline
  Load forwarding
  Memory disambiguation and its speculation

## Slide 99: Historical Perspective
1967: Tomasulo’s algorithm
~1985: history buffer
1985: Andre Pleszkun & James E Smith invented reorder buffer and future file to support precise interrupt
1987: Guri Sohi showed reorder buffer could be used for renaming and supporting speculative execution

## Slide 100: History Buffer (HB)
Operation of HB
  HB is a FIFO with head and tail pointer (like ROB)
  Instruction dispatch
    Reserve HB entry at tail, advance tail ptr
    If instruction writes register Rx, read old value of Rx from register file and save it in the HB
  Instruction execution/completion
    Write register file when instruction completes
    Updates occur out-of-order: “messy register file” (imprecise)
    If instruction caused an exception, mark exception bit in the HB for offending instruction
  Instruction retire
    Check instruction at the head of the HB
      If completed, check exception bit
      If no exception, simply advance head ptr
      If exception, restore precise register file state using the saved values in HB – “undo” the speculative updates

## Slide 101: History Buffer (cont.)
Entry | Dest | OLD VALUE | Exception | Valid | PC
1 |  |  |  |  | 
2 | F6 |  | no |  | A
3 | F2 |  | no |  | B
4 | F0 |  | yes |  | C
5 | F8 | 60 |  |  | D
6 | F10 |  |  |  | E
7 | F6 | 50 |  |  | F
8 |  |  |  |  | 
9 |  |  |  |  | 
10 |  |  |  |  | 
… |  |  |  |  | 
HB
HEAD
TAIL
F0
F2
F4
F6
F8
F10
50
60
Initial register file contents
Recover register file state
from tail to head
HB and Register File when exception reaches at HEAD
F0
F2
F4
F6
F8
F10
189
-23
Restored (precise) register file contents
F0
F2
F4
F6
F8
F10
50
60

## Slide 102: Precise Tomasulo Pipeline with HB
Update state out-of-order: imprecise!
Register
File
Reservation
Stations
Functional
Units
1
2
HB
Restore state (slowly) upon exception
EXTRA RF READ PORT

## Slide 103: HB analysis
Advantages
  Unlike ROB, no extra bypass is needed
Disadvantages
  Add another RF read port, for reading destination register (getting old value)
  Slow exception handling
    Restore precise values serially from HB to RF
    Then jump to trap handler

## Slide 104: Future File (FF)
FF operation
  Maintain two register files
    Future (“messy”) register file – imprecise Tomasulo pipeline is unchanged, future register file updated OOO
    A separate, architectural register file is updated in-order by a reorder buffer
  Exception handling
    The architectural register file always contains precise state

## Slide 105: Precise Tomasulo Pipeline with FF
Future File
Reservation
Stations
Functional
Units
1
ROB
2
Architectural File
(imprecise)
(precise)

## Slide 106: FF analysis
Advantages
  Unlike ROB, no extra bypass is needed
  Unlike HB, no extra register file read port
Disadvantages
  Slow exception handling (like HB): copy architectural file to future file, then call trap handler
  Chip area overhead (2 register files instead of 1)

## Slide 107: Recall Memory Dependences…
Dependences occur not just between register addresses, but also memory addresses: Memory Dependences, e.g.
  A: ST R1, [R2] // Mem[R2] <- R1
  B: LD R3, [R2] // R3 <- Mem[R2]
  C: LD R5, 10[R4] // R5 <- Mem[R4+10]
B is dependent on A, but is C dependent on A?
  True dependent if R4+10 = R2
  Not dependent if R4+10 != R2
Memory dependences are harder to detect because they are based on register values (instead of register IDs)

## Slide 108: Memory Data Dependences
Types of Dependences
    WAW WAR RAW
    store X load X store X
    : : :
    store X store X load X
Differences vs. register dependences
  It depends on register contents, not register IDs
  Renaming cannot be done at hardware (expensive to do in compiler)
  Affected by choice of memory consistency

## Slide 109: Memory Dependency
Stores are released to cache in order
  This preserves sequential (in-order) state in cache/memory (so that recovery from exceptions is possible)
  This takes care of output dependences
Loads access the cache out of order
  with respect to each other
  with respect to previous, pending, independent stores
  But not with respect to previous, pending, dependent stores
A load/store aliases with another load/store if their effective addresses match
Notes: Store in order: why? Precise interrupts + Multi Processors.

## Slide 110: How Loads and Stores are Handled
Store
  D stage: place on store reservation station
  EX stage: compute effective address of store
  RE stage: place in store buffer (to be release to cache)
Load
  D stage: place on load reservation station
  EX stage: compute effective address of load
  MEM stage:
    Check store buffer for dependences. If any, get data (load forwarding)
    If none, get data from cache (load bypassing, load bypasses older store)
    If it can’t be determined, stall it or speculate (memory dependence speculation)

## Slide 111: Load Forwarding

## Slide 112: Memory Disambiguation Speculation
What if aliases are rare?
  Loads don’t wait for addresses of all prior stores
  Full address comparison of stores that are ready
  Bypass if no match, forward if match
  Check all store addresses when they commit
    No matching loads – speculation was correct
    Matching unbypassed load – incorrect speculation
  Replay starting from incorrect load

## Slide 113: Speculative Memory Disambiguation

## Slide 114: Use of Prediction
If aliases are rare: static prediction
  Predict no alias every time
    Why even implement forwarding? PowerPC 620 doesn’t
  Pay misprediction penalty rarely
If aliases are more frequent: dynamic prediction
  Use PHT-like history table for loads
    If alias predicted: delay load
    If aliased pair predicted: forward from store to load
      More difficult to predict pair [store sets, Alpha 21264]
  Pay misprediction penalty rarely
Memory cloaking [Moshovos, Sohi]
  Predict load/store pair
  Directly copy store data register to load target register
  Reduce data transfer latency to absolute minimum

## Slide 115: Module 6.5: Superscalar and the Limit of ILP

## Slide 116: Objectives and Outline
Objectives:
  Understand the limit of pipelining
  Understand the concept and challenges of superscalar processing
  Understand the complexity of superscalar implementation
Outline:
  The limit of pipelining
  Superscalar concept and what each pipeline stage must do
  Techniques to support superscalar processing
  Superscalar implementation complexity

## Slide 117: Limits of Pipelining
CPU_time = IC x CPI x CT
Scalar pipelining
  CPI  1 (Flynn’s bottleneck)
   reduce CT further, increase instructions per second
Problem: limits of pipelining
  Latch overhead and clock skew
    Overhead becomes a larger component of cycle
    Pipelining eventually becomes inefficient
    Diminishing returns
  Can only break logic up so far
  Pipelining is ineffective when there are dependences
    Ex: Can pipeline L1 cache but it still takes X ns to get data out. An instruction that needs that data must wait X ns regardless of how fast you make the clock and how many stages there are.

## Slide 118: Superscalar processing
scalar = 1 instruction/cycle
superscalar: N instructions/cycle
  Increase bandwidth at each stage of the pipeline
Formal definitions versus popular usage
  Formal: superscalar applies to any multiple-issue machine
  Popular: superscalar also implies dynamic scheduling
  Statically scheduled, multiple-issue machines are popularly called VLIW – “very long instruction word”
    compiler groups multiple independent instructions into a larger package
IF | ID | EX | MEM | WB |  | 
IF | ID | EX | MEM | WB |  | 
 | IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB | 
 |  | IF | ID | EX | MEM | WB
 |  | IF | ID | EX | MEM | WB

## Slide 119: How to Get to Superscalar
Inorder scalar -> inorder superscalar
OOO scalar -> OOO superscalar

## Slide 120: New complexity
IF
  Parallel access to I$
  Instruction alignment issues
ID
  Parallel register access: highly multi-ported register file
  RAW hazard cross-checks required
    Renaming/dependence checking now more complex than RF lookup
    Must also check prior instructions in fetch group
IS/EX
  Parallel execution: replicate datapaths, FUs, etc.
MEM
  > 1 per cycle? If so, multi-ported D$
WB
  Many result buses (bypasses) and register file write ports

## Slide 121: Superscalar complexity and cycle time
The IPC / CT trade-off
  Increasing superscalar complexity can hurt cycle time
  Microarchitect must balance instr. per cycle (IPC) and cycle time (CT) to achieve best overall performance
Where complexity (potentially) impacts cycle time
Instruction
Fetch Unit
Interleaved I$ for good fetch bandwidth requires extra shift/alignment logic (more later).
I$ / branch predictor performance critical for superscalar: larger I$/predictor is slower.
Dependence
checking /
register renaming /
Register File reads
Register
File
Must cross-check dependences among newly-fetched instructions – increases rename latency.
Highly multi-ported register file increases register file read latency.
Instruction
Scheduling
Window
Exposing more parallelism requires LARGE window (e.g., 64-entry or 128-entry ROB)
Superscalar means high issue rate (multiple instructions issued per cycle)
issue latency  WINDOW SIZE  ISSUE RATE
FUs
Many, long bypasses.
Wire delay is not scaling as well as transistor delay in future technologies.
Bypasses are becoming a cycle time problem.
bypass
DISPATCH
ISSUE

## Slide 122: Superscalar evolution
Historical perspective
  1 integer + 1 floating-point
  Any 2 instructions
  Any 4 instructions
  Any “n” instructions? How far?

## Slide 123: High-bandwidth instruction fetching
branch into middle of cache line
Average fetch bandwidth < 4/cycle
Dual-port the I$ in order to read out two consecutive cache lines
Merge needed instructions together to get 4/cycle bandwidth
EXPENSIVE: true dual-porting increases area quadratically

## Slide 124: Inexpensive dual-porting: interleaving
Realization
  Don’t need to read out any two cache lines
  Just need to read out two consecutive cache lines
  Split cache into two banks: one bank holds even addresses, other holds odd addresses
  This is called 2-way interleaving or banking
  Guarantees fetching full cache line worth of instructions (if branch not encountered first!)

## Slide 125: Interleaving (cont.)
Simplified IBM POWER solution
set
+1
PC
Even Sets
Odd Sets
8 instructions
align/switch mux
4 instructions
Total cache size hasn’t changed
(1 bank = ½ cache)

## Slide 126: Dispatch and Renaming
Dependence checking must be done across instructions that are dispatched in the same cycle
Illustration [Palacharla95]
Checking dependences between N instructions: O(N^2)

## Slide 127: Issue
Issue Logic

## Slide 128: Issue
Wakeup logic
Figures’ source: Palacharla98, Smith&Sohi95

## Slide 129: Issue
Select logic

## Slide 130: Execute
Multiple functional units are needed, more units increase the bypass network complexity
Alternative: pipeline the functional unit

## Slide 131: Retirement of Load vs. Store
Recall Memory dependences
Store Queue
Load Queue

## Slide 132: Conclusions
Superscalar width increases the complexity of most OOO structures at least quadratically

## Slide 133: Module 6.6: ILP 6 - Compilation for Superscalar Execution

## Slide 134: Objectives and Outline
Objectives:
  Understand static vs. dynamic instruction scheduling
  Understand local and global scheduling
  Understand various optimizations that help ILP
Outline:
  Differences between static and dynamic scheduling and how they interact
  Local vs. global scheduling
  Loop unrolling, software pipelining, trace scheduling, and predication

## Slide 135: Static Scheduling
Have compiler re-order code to improve performance
Concepts covered
  A comparison of static and dynamic scheduling
    Each has advantages/disadvantages
    Bottom line: find good combination of the two
  Support for high-performance static scheduling
    Register pressure: large architectural register file
    Branches: compile-time region formation
    Ambiguous memory dependences: speculative loads
  Static scheduling techniques
    Local scheduling (within a basic block)
    Loop unrolling
    Software pipelining (modulo scheduling)
    Trace scheduling
    Predication

## Slide 136: Static / Dynamic Scheduling
Dynamic
Static
moderately scheduled code
FU
dynamically
re-order
instructions
statically
re-order
instructions
FU
FU
FU
moderately scheduled code
FU
FU
FU
FU
compiler
hardware
compiler
hardware
VLIW
PROCESSOR
SUPERSCALAR
PROCESSOR

## Slide 137: Local scheduling
Local scheduling = basic block scheduling
  (+) simple: no speculation (no region formation)
  (-) limited parallelism (usually < 2)
Example
Loop: LD F0, 0(R1)
(stall)
ADDD F4, F0, F2
(stall)
(stall)
SD F4, 0(R1)
ADD R1, R1, 8
BNE R1, xxx, Loop
Loop: LD F0, 0(R1)
(stall)
ADDD F4, F0, F2
ADD R1, R1, 8
(stall)
SD F4, -8(R1)
BNE R1, xxx, Loop
Loop: LD F0, 0(R1)
(stall)
ADDD F4, F0, F2
ADD R1, R1, 8
BNE R1, xxx, Loop
SD F4, -8(R1)
Assumes delayed branch
7 cycles/iteration

## Slide 138: Loop Unrolling
Unroll the loop (e.g., four times)
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD F4, 0(R1)
ADD R1, R1, 8
BNE R1, xxx, Loop
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD F4, 0(R1)
LD F6, 8(R1)
ADDD F8, F6, F2
SD F8, 8(R1)
LD F10, 16(R1)
ADDD F12, F10, F2
SD F12, 16(R1)
LD F14, 24(R1)
ADDD F16, F14, F2
SD F16, 24(R1)
ADD R1, R1, 32
BNE R1, xxx, Loop
More registers needed!
Benefits:
Less dynamic instruction overhead (SUB/BNEZ)
Less branches => larger basic block: can reschedule operations easier
Loop: LD F0, 0(R1)
LD F6, 8(R1)
LD F10, 16(R1)
LD F14, 24(R1)
ADDD F4, F0, F2
ADDD F8, F6, F2
ADDD F12, F10, F2
ADDD F16, F14, F2
SD F4, 0(R1)
SD F8, 8(R1)
SD F12, 16(R1)
SD F16, 24(R1)
ADD R1, R1, 32
BNE R1, xxx, Loop
14 cycles/4 iterations
(3.5 cycles/iteration)

## Slide 139: Loop Unrolling
Positives/negatives
  (+) larger block for scheduling
  (+) reduces branch frequency
  (+) reduces dynamic instruction count (loop overhead)
  (-) expands code size
  (-) have to handle excess iterations (“strip mining”)

## Slide 140: Software Pipelining
Treat dependent operations in a loop as a pipeline
  LD(i) -> ADDD(i) -> SD(i)
  Hide latencies by placing different stages in successive iterations
    LD(i) goes in first iteration
    ADDD(i) goes in second iteration
    SD(i) goes in third iteration
    Stated another way: LD(i), ADDD(i-1), SD(i-2) go in the same iteration
for (i=1; i<=N; i++) {
// a[i] = a[i] + k;
load a[i]
add a[i]
store a[i]
}
START-UP-BLOCK
for (i=3; i<=N; i++) {
load a[i]
add a[i-1]
store a[i-2]
}
FINISH-UP-BLOCK
 | START-UP (prologue) |  | LOOP |  |  | FINISH-UP (epilogue) | 
load | a[1] | a[2] | a[3] | a[i] | a[N] |  | 
add |  | a[1] | a[2] | a[i-1] | a[N-1] | a[N] | 
store |  |  | a[1] | a[i-2] | a[N-2] | a[N-1] | a[N]

## Slide 141: Software Pipelining
Assembly code version
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD F4, 0(R1)
ADD R1, R1, 8
BNE R1, xxx, Loop
START: LD F0, 0(R1)
ADD R1, R1, 8
ADDD F4, F0, F2
LD F0, 0(R1)
ADD R1, R1, 8
Loop: SD F4, -16(R1)
ADDD F4, F0, F2
LD F0, 0(R1)
ADD R1, R1, 8
BNE R1, xxx, Loop
FINISH: SD F4, -16(R1)
ADDD F4, F0, F2
ADD R1, R1, 8
SD F4, -16(R1)
START: LD F0, 0(R1)
ADDD F4, F0, F2
LD F0, 8(R1)
ADD R1, R1, 16
FINISH: SD F4, -16(R1)
ADDD F4, F0, F2
SD F4, -8(R1)

## Slide 142: Software Pipelining
Positives/negatives
  (+) no dependences in loop body
  (+) same effect as loop unrolling (hide latencies), but don’t need to replicate iterations (code size)
  (-) still have extra code for prologue/epilogue (pipeline fill/drain)
  (-) does not reduce branch frequency

## Slide 143: Trace Scheduling
Select most common path – a trace
  Use profiling to select a trace
  Allows global scheduling, i.e., scheduling across branches
  This is speculation because schedule assumes certain path through region
  If trace is wrong (other paths taken), execute repair code
b[i] = `old’
a[i] =
if (a[i] > 0) then
b[i] = `new’ // common case
else
X
c[i] =
Trace to be scheduled
b[i] = `old’
a[i] =
b[i] = `new’
c[i] =
if (a[i] <= 0) goto A
B:
A: restore old b[i]
X
maybe recalculate c[i]
goto B
Repair code
Original code

## Slide 144: Predication
ISA role
  Provide predicate registers
  Provide predicate-setting instructions (e.g., compare)
  Subset of opcodes can be guarded with predicates
Compiler role
  Replace branch with predicate computation
  Guard alternate paths with <predicate> and <!predicate>
Hardware role
  Execute all predicated code, i.e., both paths after a branch
  Do not commit either path until predicate is known
  Conditionally commit or squash, depending on predicate
b[i] = `old’
a[i] =
if (a[i] > 0) then
b[i] = `new’ // common case
else
X
c[i] =
Original code
b[i] = `old’
a[i] =
pred1 = (a[i] > 0)
< pred1>: b[i] = `new’
<!pred1>: X
c[i] =
Predicated code

## Slide 145: Predication
Positives/negatives
  (+) Larger scheduling scope without speculation
  (-) ISA extensions; opcode pressure, extra register specifier
  (-) May degrade performance if over-commit fetch/execute resources
  (-) Convert control dependence to data dependence
    Does this really fix the branch problem?
    Not predicting control flow delays resolving register dependences
    Can lengthen schedule w.r.t. trace scheduling
Above discussion is simplified
  Predication issues are much, much more complex…
  Complicating matters:
    S/W: trace scheduling, predication, superblocks, hyperblocks, treegions, …
    H/W: selective multi-path execution, control independence, …

## Slide 146: CDC-6600 example
DISPATCH | ISSUE | EXECUTE | WRITE RESULT
x | x | x | x
x | x | x | 
x |  |  | 
x |  |  | 
x |  |  | 
LD F6 , 34(R2)
LD F2 , 45(R3)
MULTD F0 , F2, F4
SUBD F8 , F6, F2
DIVD F10, F0, F6
ADDD F6 , F8, F2
Instruction Status
Functional Unit Status
FU | busy | op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | yes | LD | F2 | R3 |  |  |  | yes | 
MULT1 | yes | MULTD | F0 | F2 | F4 | Integer |  | no | yes
MULT2 | no |  |  |  |  |  |  |  | 
ADD | yes | SUBD | F8 | F6 | F2 |  | Integer | yes | no
DIV | yes | DIVD | F10 | F0 | F6 | MULT1 |  | no | yes
F0 | F2 | F4 | F6 | F8 | F10 | F12
MULT1 | Integer |  |  | ADD | DIV | 
Register Result Status
Notes: Instruction table describe first
Snapshot
Why two mult1?
Why add Ri yes?
The first LD is finished already in this example