## Slide 1
Prof. Jongouk Choi
University of Central Florida
Spring 2026
CDA 5106: Advanced Computer
Architecture
Lecture 3: ISA

## Slide 2: Objectives and Outline
Objectives:
  Understand the design space of ISA, their trade offs
  Able to generate code on various ISAs and analyze trade offs
  Recite key features of major ISAs
Outline (totaling 3 sub-modules)
  What is ISA?
  ISA Styles: stacks, accumulator, register-memory, load-store
  Alignment, endian-ness, instruction encoding
  Addressing modes
  Control transfer instruction types and styles
  Examples of major ISAs

## Slide 3: Module 3.1: Instruction Set Architecture1

## Slide 4: Programming language is booming up!

## Slide 5: Hardware Complexity is Blowing Up!

## Slide 6: Instruction Set Architecture
What is ISA?
  A well-define hardware-software interface
  The “contract” between software/hardware
    Functional definition of operations, addressing modes,
    and storage locations supported by hardware
ISA

## Slide 7: What is ISA?
Agreed upon interface between software and hardware
SW/compiler assumes, HW promises
What the software writer needs to know to write and debug system/user programs
Instructions: the words of a computer language
Instruction set: vocabulary
Instruction sets may differ from computer to computer, e.g., x86, arm, MIPS…, but have many things in common.
  Computational operations
  Memory access & addressing
  Branches
  Procedure calls
All instruction sets promote a common goal.
  Make it easy to build the hardware and the compiler while maximizing performance and minimizing cost.
Notes: Instruction set architecture is the agreement between hardware and software.
as long as the software follows the agreement, it can control the hardware.
[click]
instructions are the words of a computer language, and you can think it is like a vocabulary.
[click]
however, the set itself may differ from system to system.
if you target x86 intel architecture, the isa must be different.
But all systems have some common concepts
jcomputational operations.
There is always a way to access memory and handle the addressing for that.
All instruction sets support branches,
And there's also a method for procedure calls. or function calls.

## Slide 8: Example: Arithmetic Operations
Addition
add a, b, c
a = b + c; (C programming)
destination
sources
three operands
Instruction
Notes: let's first talke about the arithmetic operations with ISA.
since All hardware systems need to be able to add values.[click]
let's say we want to add b to c and store the sum into a.
that is a=b+c;[click]\
to run this operation, we need to have three operands, a destination and two sources.
The order of which are important for the language.
Our command is add, and
then our operands are listed a then b, then c,
which translates into a has been assigned the value of b plus c.[click]
this is like a R type MIpS instruction, we are going to talk about the type later.
So this is our first instruction, it is part of a classification of
instructions called R type instructions and for our R types,
they're always of this form, the name of the instruction and
then the three variables, two sources and one destination.

## Slide 9: Example: Arithmetic Operations
a = b + c + d + e
add a, b, c #a = b + c
add a, a, d #a = b + c + d
Each line can only have one instruction on it
Anything following a # is a comment.
add a, a, e #a = b + c + d + e
Notes: Let's look at a slightly more complex addition.
Let's suppose we wanted to add four things together.[click]
We'll do b plus c. Store the sum into a.[click]
And then we can take that quantity and use that as an operand for
another add operation for we'll add d on to that.
Store the sum in to a again.
And we'll use that as an operand for
the final add where we add e on to a and store the sum in a. [click]
In that way, after three add operations,
we'll have the value a value, that is b plus c plus d plus e.
So each line does a single add operation.
Any one line can only do one operation.

## Slide 10: Perspectives
Once upon a time, computer architecture = ISA design
Evolution
  pre-RISC: many different ISAs, trade-offs not well understood
  RISC: people understand trade-offs, ISA standardized
  VLIW (EPIC): the most recent big ISA design effort
  MMX, SSE: ISA multimedia extension
  Trend: new instructions to provide new capabilities, e.g.
    Decimal arithmetic in IBM Power6
    Intel SGX for secure enclaves, TSX for transactional memory support
Notes: Single instruction multiple data

## Slide 11: Why is the ISA important?
ISA decisions affect: (Revisit RISC vs. CISC…)
  Memory cost of the machine
    Short vs. long bit encodings
    high vs. low semantic meaning per instruction
  Hardware design
    Simple, uniform-complexity ops => efficient pipeline
    Don’t build hardware for instructions that never get used
  Compiler and programming language issues
    How much can compiler exploit ISA to optimize perf.
    How well does ISA support high-level lang. constructs
    Choice for hand coding vs. compiler generated code: semantics are easy to use vs. easy to generate code for

## Slide 12: Topics: ISA Design Decisions & Outline
Style of operand specification: stack, accumulator, registers, etc.
Operand access limitations
Addressing modes for operands
Semantics:
  Mix of operations supported
  Control transfers
Encoding tradeoffs
Compiler influence

## Slide 13: Styles of ISAs
Different ISA styles for assembly code: A = B+C

## Slide 17
Suppose that we would like to compute
C = A+B
A = C-B
Assume that all of A, B, C, and D are initially in memory. What is the correct sequence of instructions in the Stack ISA?

## Slide 18
Suppose that we would like to compute
C = A+B
A = C-B
Assume that all of A, B, C, and D are initially in memory. What is the correct sequence of instructions in the Stack ISA?
Push A
Push B
Add
Pop C
Push C
Push B
Sub
Pop A

## Slide 19: Why stacks, accumulators?
Stacks:
  Compact instruction format
    All calculation operations take zero operands
    E.g. Java bytecode (chosen for easy porting and low network b/w)
Accumulator:
  Also a very compact format
  Less dependence on memory than stack-based
For both:
  Compact implies memory efficient
  Good if memory is expensive
Notes: 8 bit only, out of 32 bits… stack 2, accumulator 1 value

## Slide 20: Why registers?
Faster than memory
  Latency: raw access time (once address is known)
    Cache access: 2 cycles (typical)
    Register access: 1 cycle
Allows fast reuse of values
  Compiler does “register allocation” to keep useful data close to processor
Allows flexible instruction scheduling
    (A*B) - (C*D) - (E*F)
    A*B in R1, -C*D in R2, -E*F in R3: can easily rearrange ADD instructions
  Stack or accumulator requires swaps/rotates
Notes: Don’t need register
Register pressure?
Register allocation a= b+c, d=e+f;

## Slide 21: Number of Registers?
How many?
  How many is too few?
  How many is too many?
Cons of having too many
  Instruction word becomes longer (not too serious)
  Register access time increases (if > 1 cycle, may cause slowdown?)
  Context switch time increases
Anecdotes
  X86: too few, MMX adds 8 more, x86-64 adds 8 more
Notes: What is context switch?
intel 8
arm 16 or 32

## Slide 22: Operand access limitations
Load/store (0,3)
  (+) Fixed-length instructions possible: easy fetch/decode
  (+) Simpler h/w: efficient pipeline & potentially lower CT
  (-) Higher instruction count (IC)
  (-) Fixed-length instructions are wasteful
Register/memory (1,2)
  (+) No need for extra loads
  (+) “A few lengths” better uses bits
  (-) Destroys source operand (e.g., Add R1,R2)
  (-) May impact CPI
Memory/memory
  (+) Most compact (code density)
  (-) High memory traffic (memory bottleneck)
Good code density
Notes: Load/store: fixed 32 bit, 64 bit
CPI*CC*IC
Why wasteful?
jump d

## Slide 23: Summary: Styles of ISAs
Stack ISA
  Push <Addr>, Pop <Addr>, or ALU instructions
  ALU: pop top two entries, perform ALU op, push result
Accumulator
  Load/Store/ALU <Addr>: result affects accumulator register
Reg-Mem
  Load/Store/ALU <Reg>, <Reg or Addr> (different from H&P!)
    At most one operand can be address
    Leftmost register acts as destination (if applicable)
Load-Store
  Load/Store <Reg>, <Addr>
  ALU <Reg1>, <Reg2>, <Reg3>: Reg1 is destination, Reg2, 3 are source
Notes: For acuumulator, we need a special register.

## Slide 24: Aside: Pros and cons of operand styles
Stack
  Advantages: Simple Model of expression evaluation (reverse polish). Short instructions.
  Disadvantages: A stack can‘t be randomly accessed. This makes it hard to generate eficient code. The stack itself is accessed every operation and becomes a bottleneck.
Accumulator
  Advantages: Short instructions.
  Disadvantages: The accumulator is only temporary storage so memory traffic is the highest for this approach.
Register/ load & store
  Advantages: Makes code generation easy. Data can be stored for long periods in registers.
  Disadvantages: All operands must be named leading to longer instructions.

## Slide 25: Aside: Alignment
Byte alignment
  Any access is accommodated
Word alignment
  Only accesses that are aligned at natural word boundaries are accommodated due to DRAM/SRAM organization
  Reduces number of reads/writes to memory
  Eliminates hardware for alignment (typically expensive)
  Often handle misalignment via software:
    Compiler detects & generates appropriate instructions
    …or O/S detects and runs “fixit” routine
0
memory (bytes)
1
2
3
4
5
6
7
Word size = 4 bytes
Asking for words beginning at 0 or 4 is OK
Asking for other words requires two reads
(e.g., ask for word starting at 2)
0
1
2
3
4
5
6
7
read #1
read #2
2
3
4
5
2
3
4
5
reorder
Unaligned
access
Notes: Memory is like an array of byte
Struct{
Int a
Int b
Char c
Int d;
}

## Slide 26: Aside: Endian-ness
Where is the most-significant byte (MSB) in a word?
  Little-endian (e.g., x86)
    “little”-endian comes from interpreting byte address 0 as the “least”-significant byte
  Big-endian (e.g., IBM PowerPC)
    “big”-endian comes from interpreting byte address 0 as the “most”-significant byte
Byte address
0
1
2
3
4
5
6
7
LSB
MSB
0
1
2
3
4
5
6
7
MSB
LSB
Byte address
Notes: one program compile for little-endian storing a b c d a must bt address 0
but it turns out to be big-endia, then it will read d c b a

## Slide 27: Module 3.2: Instruction Set Architecture2

## Slide 28: RISC-Style ISA
Reduced Instruction Set Computing (RISC), as opposed to Complex Instruction Set Computing (CISC)
Designed from the ground up for easy pipelining and exploitation of instruction level parallelism (ILP).
Main characteristics
  Load/store ISA: only loads/stores have a memory operand => Easy pipelining and uniform instruction width
  Fixed instruction width => easy fetch and decode
  Small number of addressing modes => easy pipelining
  Large register file => 32 int + 32 fp registers
  Aligned memory => easy data fetch
Notes: Load/store ISA ensures that there is only a need for one MEM stage in the pipeline, and only load and store use it.
Load/store ISA also ensures instruction width can be fixed. At most an instruction has one long operand (mem address)
Fixed instruction width
ILP oriented: large number of registers reduce false dependences due to reuse

## Slide 29: Common addressing modes
Register
  Add R4, R3
  R4 = R4 + R3
  Used when value is in a register
Immediate
  Add R4, #3
  R4 = R4 + 3
  Useful for small constants, which occur frequently
Displacement
  Add R4, 100(R1)
  R4 = R4 + Mem[100+R1]
  Accesses the frame (arguments, local variables)
  Accesses the global data segment
  Accesses fields of a data struct

## Slide 30: Addressing modes (cont.)
Register deferred/Register indirect
  Add R3, (R1)
  R3 = R3 + Mem[R1]
  Access using a computed address
Indexed
  Add R3, (R1 + R2)
  R3 = R3 + Mem[R1 + R2]
  Array accesses
    R1 = base, R2 = index
Direct/Absolute
  Add R1, (1001)
  R1 = R1 + Mem[1001]
  Accessing global (“static”) data
Notes: We don’t really need these

## Slide 31: Addressing modes (cont.)
Memory indirect/Memory deferred
  Add R1, @(R3)
  R1 = R1 + Mem[Mem[R3]]
  Pointer dereferencing: x = *p; (if p is not register-allocated)
Autoincrement/Postincrement
  Add R1, (R2)+
  R1 = R1 + Mem[R2]; R2 = R2 + d (d is size of operation)
  Looping through arrays, stack pop
Autodecrement/Predecrement
  Add R1, -(R2)
  R2 = R2 - d; R1 = R1 + Mem[R2] (d is size of operation)
  Same uses as autoincrement, stack push
Scaled
  Add R1, 100(R2)[R3]
  R1 = R1 + Mem[100+R2+R3*d] (d is size of operation)
  Array accesses for non-byte-sized elements

## Slide 32: Wisdom about modes
Need:
  Register, Displacement, Immediate and optionally Indexed (indexed simplifies array accesses)
  Displacement size 12-16 bits (empirical)
  Immediate: 8 to 16 bits (empirical)
  Can synthesize the rest from simpler instructions
  Example-- Mips architecture:
    Register, displacement, Immediate modes only
    both immediate and displacement: 16 bits
Choice depends on workload!
  For example, floating-point codes might require larger immediates, or 64bit wordsize machines might also require larger immediates (for *p++ kind of operations)
Notes: mentissa

## Slide 33: Only a Few Needed
RISC machines typically implement register, immediate, displacement
  i.e., load/store with only register displacement
What about other modes?
  Can be synthesized from simpler addressing modes
    e.g., memory indirect: Rj = M[M[Ri]] => Rk = M[Ri]; Rj = M[Rk]
  May increase instruction format width
    e.g. scaled requires 2 register operands plus an immediate
  May be harder to pipeline and complex to handle
    e.g. memory indirect requires two memory accesses, which may lead to two cache misses, two page faults, etc.
  R1 = R1 + Mem[Mem[R3]]
Notes: Rj = M[M[Ri]] => Rk = M[Ri]; Rj = M[Rk]

## Slide 34: Control transfer semantics
Types of branches
  Conditional
  Unconditional
    Normal
    Call
    Return
PC Relative (Branch) vs. Absolute (Jump)
  Branch allows relocatable (“position independent”) code
  Jump allows branching further than PC relative

## Slide 35: Parts of a control transfer
Where
  Determine target address
Whether
  Determine if transfer should occur or not
When
  Determine when in time the transfer should occur
Each of the three decisions can be decoupled or coupled

## Slide 36: Types of control transfer (cont).
All three: Compare and branch instruction (e.g. VAX, PA-RISC)
  Br (R1 = R2), destination
  (+) A single instruction
  (-) Heavy hardware requirement, inflexible scheduling
Whether separate from Where/When:
  Condition code register (CMP R1,R2 … BEQ dest) (x86, PowerPC, SPARC)
    (+) Sometimes test happens “for free”
    (-) Hard for compiler to figure out which instructions depend on CC register
  Condition register (SUB R1,R2 … BEQ R1, dest) (Alpha, MIPS)
    (+) Simple to implement, dependencies between instructions are obvious to compiler
    (-) Uses a register (“register pressure”)
Notes: We cannot reuse the r1 between sub and beq instruction.
R! value must be consistent in between.

## Slide 37: Prepare-to-branch Instruction
Decouple all three of Where/Whether/When
Where: PBR BTR1 = destination
  BTR1 = “Branch target register #1”
Whether: CMP PR2 = (R1 = R2)
  PR2 = “Predicate register #2”
When BR BTR1 if PR2
(+) Schedule each instruction so it happens during “free time” when hardware is idle
(-) Three instructions: higher IC
From the HP Labs PlayDoh architecture

## Slide 38: Instruction Encoding
Figure A.18 Three basic variations in instruction encoding: variable length, fixed length, and hybrid. The variable format can support any number of operands, with each address specifier determining the addressing mode and the length of the specifier for that operand. It generally enables the smallest code representation, since unused fields need not be included. The fixed format always has the same number of operands, with the addressing modes (if options exist) specified as part of the opcode. It generally results in the largest code size. Although the fields tend not to vary in their location, they will be used for different purposes by different instructions. The hybrid approach has multiple formats specified by the opcode, adding one or two fields to specify the addressing mode and one or two fields to specify the operand address.

## Slide 39: Summary: Instruction Encoding tradeoffs
Variable width
  Common instructions are short (1-2 bytes), less common or more complex instructions are long (>2 bytes)
  (+) Very versatile, uses memory efficiently
  (-) Instruction words must be decoded before number of instructions is known
  E.g. VAX, x86 (instruction can be 1-17 bytes)
Fixed width
  Typically 1 instruction per 32-bit word (Alpha is 2 instructions per word)
  (+) Every instruction word is an instruction, Easier to fetch/decode
  (-) Uses memory inefficiently
  E.g. Alpha, ARM, MIPS, PowerPC, SPARC
Hybrid
  Primarily for embedded processor to conserve memory
  Often use subset of instructions, fewer registers, or even instruction compression (IBM)
  E.g. IBM 360/370, MIPS16, ARM Thumb

## Slide 40: Module 3.3: Instruction Set Architecture Example
Notes: Project guideline

## Slide 41: RECAP: addressing modes
Register
  R4 = R4 + R3
Immediate
  R4 = R4 + 3
Displacement
  R4 = R4 + Mem[100+R1]
Register deferred/Register indirect
  R3 = R3 + Mem[R1]
Indexed
  R3 = R3 + Mem[R1 + R2]
Direct/Absolute
  R1 = R1 + Mem[1001]
Memory indirect/Memory deferred
  R1 = R1 + Mem[Mem[R3]]
Autoincrement/Postincrement
  R1 = R1 + Mem[R2]; R2 = R2 + d (d is size of operation)
Autodecrement/Predecrement
  R2 = R2 - d; R1 = R1 + Mem[R2] (d is size of operation)
Scaled
  R1 = R1 + Mem[100+R2+R3*d] (d is size of operation)
may be unnecessary

## Slide 42: RECAP: Types of control transfer (cont).
All three: Compare and branch instruction (e.g. VAX, PA-RISC)
  Br (R1 = R2), destination
  (+) A single instruction
  (-) Heavy hardware requirement, inflexible scheduling
Whether separate from Where/When:
  Condition code register (CMP R1,R2 … BEQ dest) (x86, PowerPC, SPARC)
    (+) Sometimes test happens “for free”
    (-) Hard for compiler to figure out which instructions depend on CC register
  Condition register (SUB R1,R2 … BEQ R1, dest) (Alpha, MIPS)
    (+) Simple to implement, dependencies between instructions are obvious to compiler
    (-) Uses a register (“register pressure”)
Notes: We cannot reuse the r1 between sub and beq instruction.
R! value must be consistent in between.

## Slide 43: RECAP: Prepare-to-branch Instruction
Decouple all three of Where/Whether/When
Where: PBR BTR1 = destination
  BTR1 = “Branch target register #1”
Whether: CMP PR2 = (R1 = R2)
  PR2 = “Predicate register #2”
When BR BTR1 if PR2
(+) Schedule each instruction so it happens during “free time” when hardware is idle
(-) Three instructions: higher IC
From the HP Labs PlayDoh architecture

## Slide 44: MIPS
An example of RISC ISA, designed from the ground up for easy pipelining and exploitation of instruction level parallelism.
Main characteristics
  Load/store ISA: only loads/stores can have memory operand => easy pipelining and uniform instruction width
  Fixed instruction width => easy fetch and decode
  Small number of addressing modes => easy pipelining
  Large register file => 32 int + 32 fp registers
  Aligned memory => easy data fetch
  Quantitatively designed
Notes: Load/store ISA ensures that there is only a need for one MEM stage in the pipeline, and only load and store use it.
Load/store ISA also ensures instruction width can be fixed. At most an instruction has one long operand (mem address)
Fixed instruction width
ILP oriented: large number of registers reduce false dependences due to reuse

## Slide 45: Addressing
Source:Corporaal05

## Slide 46: Instruction format
Example instructions
Instruction Meaning
add $s1,$s2,$s3 $s1 = $s2 + $s3
addi $s2,$s3,4 $s2 = $s3 + 4
lw $s1,100($s2) $s1 = Memory[$s2+100]
bne $s4,$s5,L if $s4<>$s5 goto L
j Label goto Label
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J
Source:Corporaal05
Notes: Notice opcode “addi” encodes the immediate addressing mode

## Slide 47: Pipelining
time
Instruction stream
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
All integer instructions fit into the following pipeline
Source:Corporaal05

## Slide 48: Case Study: x86
X86 = Instruction set architecture originating from Intel 8086
  Designed “quickly” as processors for first IBM PC
    IBM required second sourcing (hence Intel & AMD)
  Most popular today, despite drawbacks
  Has been implemented in processors made by Intel, AMD, Cytrix, VIA, etc.
  Started off as 16-bit (1978), then 32-bit (1985), 64-bit (1999)
  Over the years, new instructions were added, more registers were added

## Slide 49: x86 Registers: too few
AH
AL
BH
CH
DH
BL
CL
DL
AX
BX
CX
DX
8
8
16
EAX
EBX
ECX
EDX
ESI
EDI
EBP
ESP
CS
SS
DS
ES
FS
GS
EIP
general
purpose
registers
index
registers
pointer
registers
segment
registers
PC
condition codes (a.o.)
Source:Corporaal05
Notes: https://www.eecg.utoronto.ca/~amza/www.mindsec.com/files/x86regs.html

## Slide 50: Example Usage
Addressing Modes
Simple Example
Void MyFunction()
{
int a, b, c;
a = 10;
b = 5;
c = 2;
}
push ebp ; save ebp
mov ebp, esp ; ebp points to TOS
sub esp, 12 ; allocate local vars
mov [ebp-4], 10
mov [ebp-8], 5
mov [ebp-12], 2
Notes: Ebp: base pointer return address
Esp: stack pointer
Scaled

## Slide 51: Condition Code
Flag | Name | Description
Z | Zero flag | Indicates that the result of arithmetic/logical operation is zero
C | Carry flag | Indicates that an operation has a carry out. Enables numbers larger than a single word to be added/subtracted
S/N | Sign/negative flag | Indicates that the result of an operation is negative.
V/O/W | Overflow flag | Indicates that the result of an operation is too large to fit in a register (using two’s complement representation)
Subsequent conditional branch may test condition code
to determine whether it should be taken/not taken

## Slide 52: X86 is Evolving: New Instructions
MMX (1996)
SSE (1999) - Pentium III
SSE2 (2001) - Pentium 4
SSE3 (2004)
SSSE3 (2006) - Intel Core
SSE4 (2006)
AVX (2011) - Sandy Bridge
AVX2 (2013) - Haswell (successor of Ivy Bridge)
SGX, MPX, SHA (2015) -
SME – Secure Memory Extension
TME - Total Memory Encryption

## Slide 53: Aside: Additional Registers
Pentium MMX added:
  Eight 64-bit MMX integer registers (MMX0 to MMX7)
Pentium III added:
  Streaming SIMD Extensions (SSE) status register (MXCSR)
  Eight 128-bit SSE floating point registers (XMM0 to XMM7)
64-bit mode added:
  Eight 64-bit general registers (R8-R15)
  R-prefix replaces E-prefix for other registers, e.g. RAX, RBX
SIMD extension added
  128-bit registers, 256-bit registers, and 512-bit registers

## Slide 54: Exercise
Explain each line of the following MIPS code and describe in a sentence or two what it computes. Assume that $a0 is used for the input and initially contains n (let’s say 10), a positive integer. Assume that $v0 is used for returning the output value.
What is the expected result in $v0 from this code?
begin: addi $t0, $zero, 0
addi $t1, $zero, 1
loop: slt $t2, $a0, $t1 bne $t2, $zero, finish
add $t0, $t0, $t1
addi $t1, $t1, 2 j loop
finish: add $v0, $t0, $zero

## Slide 55: Exercise (Solution)
Explain each line of the following MIPS code and describe in a sentence or two what it computes. Assume that $a0 is used for the input and initially contains n (let’s say 10), a positive integer. Assume that $v0 is used for returning the output value.
What is the expected result in $v0 from this code?
begin: addi $t0, $zero, 0 // initialize $t0 = 0
addi $t1, $zero, 1 // initialize $t1 = 1
loop: slt $t2, $a0, $t1 // is n < $t1? bne $t2, $zero, finish // if so, then go to finish
add $t0, $t0, $t1 // else $t0 = sum of odd numbers < n
addi $t1, $t1, 2 // increment $t1 by 2 j loop // repeat loop
finish: add $v0, $t0, $zero // return $t0 in $v0
1 + 3 + 5 + ... + n (or n – 1 if n is even)
1 + 3 + 5 + 7 + 9 = 25

## Slide 56: Further Study…

## Slide 57: Using Condition Code in a Branch
Special instruction: compare
    CMP SRC1,SRC2 ; set (Z,O,C,S) based on SRC1-SRC2
Example
    for (i=0; i<10; i++)
    a[i]++;
  MOV EAX,0 ; EAX = i = 0
  _L: CMP EAX,10 ; performs EAX-10, set CC’s
  JNL _EXIT ; jump if not less to _EXIT
  INC [EBX] ; Mem[EBX](=a[i])++
  ADD EBX,4 ; EBX = &a[i+1]
  INC EAX ; EAX++
  JMP _L ; goto _L
  _EXIT: ...
Source:Corporaal05

## Slide 58: Example of Adding Vectors
// A 16byte = 128bit vector struct
struct Vector4
{
float x, y, z, w;
};
// Add two constant vectors and return the resulting vector
Vector4 SSE_Add ( const Vector4 &Op_A, const Vector4 &Op_B )
{
Vector4 Ret_Vector;
__asm
{
MOV EAX Op_A // Load pointers into CPU regs
MOV EBX, Op_B
MOVUPS XMM0, [EAX] // Move unaligned vectors to SSE regs
MOVUPS XMM1, [EBX]
ADDPS XMM0, XMM1 // Add vector elements
MOVUPS [Ret_Vector], XMM0 // Save the return vector
}
return Ret_Vector;
}

## Slide 59: Example of SSE
Parallel Scalar
ADDPS ADDSS - Adds operands
SUBPS SUBSS - Subtracts operands
MULPS MULSS - Multiplys operands
DIVPS DIVSS - Divides operands
SQRTPS SQRTSS - Square root of operand
MAXPS MAXSS - Maximum of operands
MINPS MINSS - Minimum of operands
RCPPS RCPSS - Reciprical of operand
RSQRTPS RSQRTSS - Reciprical of square root of operand
Notes: 16 byte