## Slide 1
Prof. Jongouk Choi
University of Central Florida
Spring 2026
CDA 5106: Advanced Computer
Architecture
Lecture 4: Processor

## Slide 2: Objectives and Outline
Reading: H&P, Appendix C and Chapter 3
Objectives:
  Understand basic pipeline design and its performance
  Understand hazards
  Understand various types of branch prediction, and key branch predictors
Outline:
  Module 4.1: pipeline design
  Module 4.2: branch prediction
  Module 4.3: more on branch prediction
  Module 4.3: dependence hazards and pipeline performance

## Slide 3
Module 4.1: Pipelining 1

## Slide 4: Objectives and Outline
Objectives:
  Understand basic 5-stage pipeline
  Understand various hazards (data, structural, control) and how they cause pipeline stalls
  Derive timing table for a set of instructions & pipeline design
Outline:
  5-stage pipeline design
  Various hazards (data, structural, control)
  How hazards cause stalls, and how stalls
  Extending pipeline for FP instructions

## Slide 5: Instruction Level Parallelism
ILP is a set of techniques that allows multiple instructions to be processed in parallel.
Contributes substantially to performance growth of processors in the last few decades
Key Techniques
  Pipelining
  Branch prediction
  Superscalar execution
  Out-of-order engine

## Slide 6: How to Execute an Instruction
Instruction fetch (“IF”)
  IR = Mem[PC]
  NPC = PC + 4
Instruction decode/Register fetch (“ID”)
  A = Regs[IR6..10]
  B = Regs[IR11..15]
  Imm = sign-extend(IR16..31)
Execute (“EX”)
  Memory reference: ALUOutput = A + Imm
  Reg/Reg ALU Operation: ALUOutput = A op B
  Reg/Immediate ALU Operation: ALUOutput = A op Imm
  Branch: ALUOutput = NPC + Imm; Cond = (A op 0)
Notes: For EX
Base addressing mode, ld r1 100(r2)
Add r1 r2 r3
Addi r1 r2 100
bne $t2, $zero, finish branch condition outcome is determined in stage 3.

## Slide 7: Executing an Instruction (cont.)
Memory Access/Branch completion (“MEM“)
  Memory Reference:
    Load_Mem_Data = Mem[ALUOutput] /* Load */
    Mem[ALUOutput] = B /* Store */
  Branch
    If (cond) PC = ALUOutput, else PC = NPC
Write back (“WB”)
  Reg-Reg ALU Operation:
    Regs[IR16..20] = ALUOutput
  Reg-Immediate ALU Operation:
    Regs[IR11..15] = ALUOutput
  Load instruction:
    Regs[IR11..15] = Load_Mem_Data
Notes: For WB
Add r1 r2 r3
Addi r1 r2 100
ld r1 100(r2)

## Slide 8
ALU
Instruction
cache
PC
NPC
IR
(inst.
reg.)
Regs
sign
extend
A
B
ALU
MUX
MUX
=0?
cond
MUX
data
cache
LMD
MUX
4
Imm
Instruction Fetch (IF)
Instruction Decode (ID)
Execute (EX)
Memory (MEM)
Writeback (WB)
Notes: Sign extension ALU takes only 32bit data,
what if addi r1 r2 1? 1 becomes 00000001
add r1 r2 r3
Addi r1 r2 1
datapath

## Slide 9: Example: Analysis (non-pipelined)
All instructions (except branch):
  IF, ID, EX, MEM, WB
Branch: (12%)
  IF, ID, EX, MEM
CPI = 5*0.88+4*0.12 = 4.88 cycles
Graphically:
IC
Reg
ALU
DC
Reg
IC
Reg
ALU
DC
Reg
IC
Reg
ALU
DC
Reg

## Slide 10: Pipelined DLX
Isolate each of IF, ID, EX, MEM, WB with latches
When instruction i is in WB, i+1 is in MEM, etc.
Graphically:
IC
Reg
ALU
Reg
DC
IC
Reg
ALU
Reg
DC
IC
Reg
ALU
Reg
DC
IC
Reg
ALU
Reg
DC
IC
Reg
ALU
Reg
DC
time
i
i+1
i+2
i+3
i+4

## Slide 11: Pipeline speedup (no stalls)
For a pipeline of n stages:
IF
ID
EX
MEM
WB

## Slide 12: Pipeline hazards
A hazard reduces the performance of the pipeline
  Due to program’s characteristics
Three kinds:
  Data hazards - Dependencies between instructions prevent their overlapped execution
  Structural hazards - not enough hardware resources for all combinations of instructions
  Control hazards - Branches change the PC, which results in late code

## Slide 13: Structural hazards
Uncommon for our pipeline example
Consider a pipeline with a unified data+instruction cache:
A (a load)
B
C
D
make D wait
E
IF
ID
MEM
EX
WB
time->
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
IF
ID
MEM
EX
WB
stall
IF
ID
MEM
EX
WB
ld r1, 100(r2)

## Slide 14: Modeling stalls
Ex:
  n = 5 (e.g., DLX pipeline)
  20% of instructions are branches
  60% of branches are taken
  Penalties:
    Taken branches: 3 stall cycles
    Not-taken branches: 0 stall cycles
How many stall cycles per instr. on average?
  stall cycles/instr. = (0.8 x 0) + (0.2 x [ 0.6 x 3 + 0.4 x 0]) = 0.2 x 0.6 x 3 = 0.36
  Speedup = 5 / 1.36 = 3.68
Notes: We are going to measure the penalty caused by branch.
Non-pipelined cpi was 5, pipelined cpi is 1

## Slide 15: Example
Consider the following code:
On DLX/RISC five-stage pipeline show the timing of the first iteration of the loop. Assume
  Full forwarding or bypassing
  Conditional branch is evaluated at the decode stage.
  Fetch of the target instruction is delayed until the branch direction is known.
Loop: LD R1,0(R2) ;load R1 from address 0+R2
DADDI R1,R1,#1 ;R1=R1+1
SD 0(R2),R1 ;store R1 at address 0+R2
DADDI R2,R2,#4 ;R2=R2+4
DSUB R4,R3,R2 ;R4=R3-R2
BNEZ R4,Loop ;branch to Loop if R4=!0

## Slide 16: Answer:
Instructions | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
LD R1, 0(R2) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
DADDI R1, R1, #1 |  | F | D | - | X | M | W |  |  |  |  |  |  | 
SD 0(R2), R1 |  |  | F | - | D | X | M | W |  |  |  |  |  | 
DADDI R2, R2, #4 |  |  |  |  | F | D | X | M | W |  |  |  |  | 
DSUB R4, R2, R2 |  |  |  |  |  | F | D | X | M | W |  |  |  | 
BNEZ R4, Loop |  |  |  |  |  |  | F | - | D | X | M | W |  | 
2nd iter: LD R1, 0(R2) |  |  |  |  |  |  |  | - | = | F | D | X | M | W
Notes: Data hazard
Structure hazard
Control hazard

## Slide 17
Module 4.2: Pipelining 2

## Slide 18: Schedule
Quiz: Feb. 20 (online, all day)
Midterm: Feb. 25 (in-class, 6pm-7:15pm)

## Slide 19: Objectives and Outline
Objectives:
  Understand how control hazard affect pipeline performance
  Understand how to predict branch and its target
  Understand how to predict outcome of a branch
Outline:
  Performance impact of control hazards
  Branch Target Buffer (BTB) and Return Address Stack (RAS)
  Dynamic branch predictors: 1-bit, Smith n-bit, McFarling’s GShare

## Slide 20: Control Hazards
NPC = PC+4 not always the brightest choice
Solution: use branch prediction. But what to predict?
A
B
IF
ID
MEM
EX
WB
IF
ID
-
EX
-
A BEQZ R1, G
IF
ID
-
-
-
C
IF
ID
MEM
EX
WB
G
D
IF
-
-
-
-

## Slide 21
ALU
Instruction
cache
PC
NPC
IR
(inst.
reg.)
Regs
sign
extend
A
B
ALU
MUX
MUX
=0?
cond
MUX
data
cache
LMD
MUX
4
Imm
Instruction Fetch (IF)
Instruction Decode (ID)
Execute (EX)
Memory (MEM)
Writeback (WB)

## Slide 22: Move branch target back
ALU
Instruction
cache
PC
NPC
IR
(inst.
reg.)
A
ALU
MUX
data
cache
LMD
MUX
4
=0?
cond
MUX
Instruction Fetch (IF)
Instruction Decode (ID)
Execute (EX)
Memory (MEM)
=0?
cond
MUX
ALU
Add an ALU
May increase time for ID
Eliminates 2 cycles, but still 1 additional stall
RF
Notes: Earlier pipeline stage

## Slide 23: Branch Prediction: Eliminating Control Hazard Stalls
When
  Detect an undecoded instruction is a branch
Where
  Predicting where the branch will go (if taken)
Whether
  (For conditional branches) Predict if it will branch or not, before execution
Optimal: try to determine all three in IF stage
  Won’t work perfectly (prediction), but we can try our best
Notes: Why IF? Because in the next clock cycle, we are gong to fetch the next instruction.
What is the next instruction?

## Slide 24: Issues with When and Where
What does IF know?
  Only the address of the instruction (PC)
  Keep buffer (cache) of last known branch targets around
  Buffer is written to by WB stage
Last
known
branches
PC value
Hit = we know it is a branch (“WHEN”),
BTB returns branch target (“WHERE”)
Miss = assume not a branch
Traditional name for this is a Branch Target Buffer (BTB)
tag
pre-computed target
BTB entry:

## Slide 25: Aside: Predicting Where with returns
Problem: A lot of branches are returns from procedures
  Holding the last target address is a poor predictor
Solution: Keep a hardware “stack” of return addresses
  Push return address when a “call” is executed
  Pop buffer on returns to get prediction
    Bottom of stack is filled with old value on a pop
  Need approx 4-8 entries for integer code
return?
Each entry
in BTB now
contains:
tag
pre-computed target
Notes: Extend BTB
Recursive function?
Push push push… aside

## Slide 26: Issues with Whether: Hardware branch prediction
1-bit schemes:
  Add 1-bit prediction field to branch target buffer
  Set prediction field = 1 if branch was taken, 0 if branch was not taken
  At IF, check “branch prediction buffer”:
    if prediction field = 1 then predict taken
    else predict not-taken
  Problems:
    Some branches don’t do what they did last time!
    Need more sophisticated predictor

## Slide 27: Smith n-bit counter predictor
Replace prediction bit with n-bit counter:
11
10
01
00
T
T
T
T
N
N
N
N
predict taken
predict not-taken
initial state
(using NT
heuristic)
Problems with n > 2 to 3
Smith called it “inertia”
2-bit counter
Notes: 100 taken 1 not taken
No gain beyond 2 bit,,, all current

## Slide 28: Example of Smith counter
previous state
new state
T
T
01
10
11
11
11
11
11
10
11
11
10
01
00
00
00
00
00
00
01
T
T
T
T
N
T
T
N
N
N
N
N
N
N
N
T
T
11
11
11
11
11
10
11
11
10
01
00
00
00
00
00
00
01
10
10
5 mispredictions out of 19 branch executions
T
N
T
N
T
N
T
N
T
N
T
N
T
N
T
N
T
N
01
10
01
10
previous state
new state
01
10
01
10
19 mispredictions out of 19: the infamous “toggle branch”
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10
01
10

## Slide 29: Effectivenss of 2-bit Predictor
Misprediction rate ~11% integer apps, 4% fp apps
Figure C.19 Prediction accuracy of a 4096-entry 2-bit prediction buffer for the SPEC89 benchmarks. The misprediction rate for the integer benchmarks (gcc, espresso, eqntott, and li) is substantially higher (average of 11%) than that for the floating-point programs (average of 4%). Omitting the floating-point kernels (nasa7, matrix300, and tomcatv) still yields a higher accuracy for the FP benchmarks than for the integer benchmarks. These data, as well as the rest of the data in this section, are taken from a branch-prediction study done using the IBM Power architecture and optimized code for that system. See Pan, So, and Rameh [1992]. Although these data are for an older version of a subset of the SPEC benchmarks, the newer benchmarks are larger and would show slightly worse behavior, especially for the integer benchmarks.

## Slide 30: Example
Old Counter State | Prediction Direction | Actual Outcome | Mispredicted? | New Counter State
00 | N | T | y | 01
[A1] | [B1] | T | [C1] | [D1]
[A2] | [B2] | T | [C2] | [D2]
[A3] | [B3] | N | [C3] | [D3]
[A4] | [B4] | N | [C4] | [D4]
Suppose we have a conditional branch that has an outcome shown in the table. What are the instances of the branch that will be correctly predicted using 2-bit prediction counter? Show the old counter state, prediction generated by the predictor, whether the prediction is correct, and the new state of the counter (after updated by the outcome of the current branch).
Show the prediction outcome for 2-bit counter.
Show the prediction outcome for 2-bit counter. Use T/N for 'Prediction Direction' and y/n for 'Mispredicted?'

## Slide 31: Example
Old Counter State | Prediction Direction | Actual Outcome | Mispredicted? | New Counter State
00 | N | T | y | 01
[01] | [N] | T | [y] | [10]
[A2] | [B2] | T | [C2] | [D2]
[A3] | [B3] | N | [C3] | [D3]
[A4] | [B4] | N | [C4] | [D4]
Old Counter State | Prediction Direction | Actual Outcome | Mispredicted? | New Counter State
00 | N | T | y | 01
[01] | [N] | T | [y] | [10]
[10] | [T] | T | [n] | [11]
[A3] | [B3] | N | [C3] | [D3]
[A4] | [B4] | N | [C4] | [D4]

## Slide 32: Example
Old Counter State | Prediction Direction | Actual Outcome | Mispredicted? | New Counter State
00 | N | T | y | 01
[01] | [N] | T | [y] | [10]
[10] | [T] | T | [n] | [11]
[11] | [T] | N | [y] | [10]
[A4] | [B4] | N | [C4] | [D4]
Old Counter State | Prediction Direction | Actual Outcome | Mispredicted? | New Counter State
00 | N | T | y | 01
[01] | [N] | T | [y] | [10]
[10] | [T] | T | [n] | [11]
[11] | [T] | N | [y] | [10]
[10] | [T] | N | [y] | [01]

## Slide 33: Improving the Smith Counter
Often branches exhibit correlated behavior
Example:
In the example, if the neither b1 or b2 are taken, then b3 will be taken. In other words, branch b3 behavior depends on other branches
If (aa ==2)
aa = 0;
if (bb == 2)
bb = 0;
If (aa != bb) {
addi x3, x1, -2
bnez x3, L1 // b1 (aa!=2)
add x1, x0, x0
L1: addi x3, x1, -2
bnez x3, L2 // b2 (bb!=2)
add x2, x0, x0
L2: sub x3, x1, x2
beqz x3, L3. // b3 (aa!=bb)

## Slide 34: McFarling’s Gshare Correlating Predictor
Idea:
  Capture correlations between branches (“gshare”)
  Associate predictions with branch histories, not branch addresses (use different indexing scheme)
Gshare:
global branch history register
n-1
0
behavior of last branch
(shift in most recent outcome)
index
(using low order
bits of address)
...
each entry is a two-bit counter
(or perhaps simpler)
BHR

## Slide 35: Gshare example
1
0
BHR
matrix
00
01
10
11
A: BEQZ R1, D
D: BEQZ R1, F
F: NOT R1,R1
G: JUMP A
initially R1 = 0
...
...
A: T, pred N
New BHR = 01
D: T, pred N
New BHR = 11
01
01
01
01
A:
D:
BHR = 00
01
01
01
01
00
01
10
11
10
01
01
01
A:
D:
BHR = 01
01
01
01
01
00
01
10
11
10
01
01
10
A:
D:
BHR = 11
01
01
01
01
00
01
10
11
A: N, pred N
New BHR = 10
D: N, pred N
New BHR = 00
A: T, pred T
New BHR = 01
10
01
01
10
A:
D:
BHR = 10
01
01
01
00
00
01
10
11
10
01
01
10
A:
D:
BHR = 00
00
01
01
00
00
01
10
11
11
01
01
10
A:
D:
BHR = 01
00
01
01
00
00
01
10
11
D: T, pred T
New BHR = 11
11
01
01
11
A:
D:
BHR = 11
00
01
01
00
00
01
10
11
11
01
01
11
A:
D:
BHR = 10
00
01
01
00
00
01
10
11
A: N, pred N
New BHR = 10
underlined means entry
was updated due to last
branch execution
Notes: BHR, if it is taken, left shit +1, if it is not taken, left sifht + 0

## Slide 36
Module 4.3: Pipelining 3

## Slide 37: Objectives and Outline
Objectives:
  Understand various dynamic branch predictors
Outline:
  Dynamic branch predictors: Yeh/Patt predictor, Hybrid/tournament predictor, Seznec TAGE predictor
  Static branch predictors: heuristics-based, Ball/Larus, profile-based
  Case study of PowerPC 604 branch prediction structures

## Slide 38: Yeh/Patt predictor
pattern table
2-bit counters
(indexed by history
pattern)
1110111
shift registers
history table
01
address of
branch
Notes: Some branches can depend on themselves…

## Slide 39: Yeh/Patt Example: toggle branch
A: TNTNTNTNTNTNTNTNTNTN
B: TTTTTTTTTTTTTTTTTTTTTT
01
01
01
01
PT
00
00
00
00
HT
00
01
10
11
A:
B:
A: T, pred N
10
01
01
01
PT
01
00
00
00
HT
00
01
10
11
A:
B:
11
01
01
01
PT
01
01
00
00
HT
00
01
10
11
A:
B:
B: T, pred T
11
00
01
01
PT
10
01
00
00
HT
00
01
10
11
A:
B:
A: N, pred N
B: T, pred N
11
01
01
01
PT
10
11
00
00
HT
00
01
10
11
A:
B:
11
01
10
01
PT
01
11
00
00
HT
00
01
10
11
A:
B:
A: T, pred N
B: T, pred N
11
01
10
10
PT
01
11
00
00
HT
00
01
10
11
A:
B:
A: N, pred N
11
00
10
10
PT
10
11
00
00
HT
00
01
10
11
A:
B:
11
00
10
11
PT
10
11
00
00
HT
00
01
10
11
A:
B:
B: T, pred T
A: T, pred T
11
00
11
11
PT
01
11
00
00
HT
00
01
10
11
A:
B:
PT entries 01, 10 are “trained” for A
and 11 is “trained” for B
In general: provides 96-98% accuracy for integer code

## Slide 40: Hybrid/Tournament Predictors
Both predictors supply a prediction-- pipeline uses only one
Chooser updated based on which predictor was correct
  Increment chooser counter if #1 was correct, decrement if #2 was correct
Predictor
#1
(e.g., gshare)
Predictor
#2
(eg, bimodal)
Chooser
array of 2bit
counters
address of
branch
prediction

## Slide 41: Accuracy of Various Predictors
Figure 3.4 The misprediction rate for three different predictors on SPEC89 as the total number of bits is increased. The predictors are a local 2-bit predictor, a correlating predictor that is optimally structured in its use of global and local information at each point in the graph, and a tournament predictor. Although these data are for an older version of SPEC, data for more recent SPEC benchmarks would show similar behavior, perhaps converging to the asymptotic limit at slightly larger predictor sizes.

## Slide 42: Aside: Seznec’s TAGE Predictor [2006]
Winner of last several years of branch predictor competition
Multiple predictors with varied history lengths (T0..T4)
Tag is used: prediction generated if tag matches
  Final prediction = from predictor with the longest history that matches tag
  Mispred rate ~half of gshare

## Slide 43: Can Compiler Help Predict Branch?
Heuristic #1: Branches are not taken
  The majority of conditional branches are not taken
  True about 60% of the time
Heuristic #2: backward branches are taken, forward branches are not taken (BTFNT)
  Theme: Most backward branches are loops
  Notes:
    Since branches are PC relative, sign bit of offset = the prediction
    Jim Smith reports 70% accuracy for this scheme for scientific workloads
Heuristic #3: Ball/Larus style predictions
  Set of rules to predict branches in special situations

## Slide 44: Examples of Ball/Larus predictions
Detect loops and use BTFNT
Since error values returned by library functions are negative:
  …and since errors are rare
  Predict BLTZ, BLEZ, etc. not taken
  Predict BGTZ, BGEZ, etc., taken
If a call is in the body of an if…then, predict the “then” branch as not-taken
  Since most calls in if…thens guard special case code
Problem:
  Works great for SPECint92 (from which it was designed)
  My code might not work like that!
Notes: Branch less than zero
Branch grater than zero

## Slide 45: Profiling
Three steps:
  1. Run the program [the “profiled run”]
  2. Record the preferred direction for each branch (T or NT)
  3. Recompile to set the likely bits
What if the program takes inputs (e.g., sort)?
  Collect a representative set of inputs somehow
Problems:
  One prediction for entire run
  The profiled run is slow!

## Slide 46: Effectiveness of Static Predictor
Reasonable accuracy, but misprediction higher than dynamic predictors
Figure C.17 Misprediction rate on SPEC92 for a profile-based predictor varies widely but is generally better for the floating-point programs, which have an average misprediction rate of 9% with a standard deviation of 4%, than for the integer programs, which have an average misprediction rate of 15% with a standard deviation of 5%. The actual performance depends on both the prediction accuracy and the branch frequency, which vary from 3% to 24%.

## Slide 47
Module 4.4: Pipelining 4

## Slide 48: Objectives and Outline
Objectives:
  Understand various types of dependences (RAW/WAR/WAW) and (register vs. memory)
  Draw data dependence graph given a set of instructions
  Understand data forwarding (bypassing network)
  Analyze pipeline performance through loop analysis
Outline:
  Various data dependences and dependence graph
  Data forwarding (bypassing network) impact on pipeline
  Pipeline loop analysis
  Case studies of example commercial processor pipelines

## Slide 49: Let’s Revisit Types of dependencies
True-dependence (pure-dependence, flow-dependence)
  ADD R1,R2,R3
  SUB R4,R5,R1
  May cause RAW hazards
Anti-Dependence
  ADD R3,R2,R1
  SUB R1,R4,R5
  May cause WAR hazards
  Due to reuse: Removed by using another register
Output-Dependence
  ADD R1,R2,R3
  SUB R1,R4,R5
  May cause WAW hazards
  Due to reuse: Removed by using another register

## Slide 50: Dependence Graph
Example
  A: ADD R1,R2,R3
  B: SUB R4,R5,R1
  C: ADD R6,R1,R4
  D: MUL R3,R7,R8
  E: DIV R4,R9,R10

## Slide 51: Aside: Memory Dependences
Dependences occur not just between register addresses, but also memory addresses: Memory Dependences, e.g.
  A: ST R1, [R2] // Mem[R2] <- R1
  B: LD R3, [R2] // R3 <- Mem[R2]
  C: LD R5, 10[R4] // R5 <- Mem[R4+10]
B is dependent on A, but is C dependent on A?
  True dependent if R4+10 = R2
  Not dependent if R4+10 != R2
Dependences harder to detect because they are based on register values, rather than register addresses
Will discuss in greater details in a later module

## Slide 52: Data hazard
Read-after-write (RAW) hazard
IF
add r1, r2, r3
ID
IF
add r4, r1, r5
EX
ID
IF
MEM
stall
stall
WB
stall
stall
ID
IF
EX
ID
WB
MEM
MEM
EX
value available
value needed
value written

## Slide 53: Data forwarding (bypasses)
ALU
D$
MUX
MUX
B
A
IMM
MUX
ID/EX
EX/MEM
MEM/WB
RF
bypass 1
bypass 2
bypass 3

## Slide 54: Data forwarding (cont.)
IF
add r1, r2, r3
ID
IF
add r4, r1, r5
WB
MEM
WB
MEM
EX
WB
EX
ID
IF
add r6, r1, r5
MEM
EX
ID
IF
add r7, r1, r5
byp 1
WB
MEM
EX
ID
IF
add r8, r1, r5
byp 2
WB
MEM
EX
ID
byp 3

## Slide 55: Stalls due to data hazards
Our simple pipeline
  Most RAW hazards => no stall
  Loads cause 1-cycle stall (cache hit)
IF
lw r1, 0(r2)
ID
IF
add r4, r1, r5
EX
ID
IF
MEM
stall
stall
WB
MEM
MEM
EX
value available
value needed
WB
EX
ID
byp 2

## Slide 56: Other data hazards
WAR (write-after-read)
  A r1, r2, r3
  B r2, r4, r5
  Hazard if B writes R2 before A reads R2
  Doesn’t happen in simple DLX pipeline, but can in others
    E.g., occurs if pipeline allows late register reads
SW 0(R2), R1 IF ID EX MEM1 MEM2 MEM3 WB
ADD R1, R3, R4 IF ID EX WB
writes R1 during WB
Reads R1 during MEM3

## Slide 57: Other data hazards (cont.)
WAW (write-after-write)
  A r1, r2, r3
  B r1, r4, r5
  Hazard if B writes R1 before A writes R1
  Result: later instructions see wrong value in the register
  Occurs if instructions can write register file out-of-order
  This also doesn’t happen in simple DLX pipeline, but can in others:
LW R1, 0(R2) IF ID EX MEM1 MEM2 WB
ADD R1, R2, R3 IF ID EX WB
writes 1st version of R1
writes 2nd version of R1

## Slide 58: Other data hazards (cont.)
Handling WAR/WAW hazards
  Stall the later instruction (stalls in WB stage)
  Compiler: don’t reuse register specifier
  Hardware: register renaming (see next major topic – ILP)

## Slide 59: Pipeline Performance
Pipeline performance depends on hazards
Pipeline loop analysis helps analyze pipeline performance
  Evaluating impact of design changes
  Identifying techniques needed to improve performance
Important for analysis: loop types and loop size
  ALU Loop: loop for dependent ALU instructions
    Size of loop: stage when value is produced – when needed
  Load-to-use Loop: loop for inst dependent on a load inst
    Size of loop: stage when value is read out from cache – when needed
  Branch misprediction Loop: loop for when a conditional branch is mispredicted
    Size of loop: when branch is resolved – fetch stage
Notes: pipeline is good for performance improvment
however, it can hazards
to avoid hazards, we have bypass paths in the pipelines.
When we design our pipeline, we should also considier the bypass paths and their impact on performance.

## Slide 60: Example
Without Data Forwarding
  ALU Loop size = 4
  Load-to-use Loop = 4
  Branch Loop = 3
With Data Forwarding
  ALU Loop size = 1
  Load-to-use Loop = 2
  Branch Loop = 3

## Slide 61: Case 1: Deep Pipeline
  ALU Loop size = 2 (was 1)
  Load-to-use Loop = 4 (was 2)
  Branch Loop = 6 (was 3)
Thus, deepening the pipeline also increases the critical loop size
  Benefit primarily comes when instructions do not have dependences, or when branches are easy to predict
  Diminishing return from deepening the pipeline

## Slide 62: Case 2: RISC vs. CISC Pipeline
CISC
  Assume CISC instruction decoded and broken into small RISC-like instructions (e.g. Macro Op -> Micro Op)
  Question: is there a cost for doing this vs. RISC?
  ALU Loop and Load-to-use Loop have the same size as RISC
  But Branch Loop = 4 (vs. 3 in RISC) => branch misprediction is costlier
Thus, everything else the same, must compensate with a better branch predictor

## Slide 63: Case 3: Increasing the L1Cache Size
Larger L1 Data Cache Size
  Suppose doubling the size adds 1 additional cycle (one extra “M2” stage)
  Question: what is the performance cost for doing this?
  Load-to-use Loop is now 3 cycles (was 2 cycles)
Thus, worse performance for instructions dependent on the loads
  Can compensate by scheduling the loads early
  May also avoid increasing L1 cache size further, back it up with a large L2 cache instead

## Slide 64: Case Study: Intel 486
486:
  1989: first pipelined implementation of x86 processor (1M transistors)
  CPI improved from 4.9 (386) to 1.95 (486)
5 Pipeline Stages
  IF: fetch instruction from 32-byte prefetch queue
  ID1: translate instruction into control signals or microcode, initiate address generation and memory access
  ID2: access microcode memory. Output microinstruction to execute unit
  EX: execute ALU and memory accessing operations (Note: Mem is folded into EX)
  WB: write back result to register

## Slide 65: Other Examples
P5, P6, and NetBurst
Atom

## Slide 66: Other Examples
Power4
ARM A7 and A15

## Slide 67: Other Examples

## Slide 68: Other Examples